## Slide 1: LhARA the Laser-hybrid Accelerator for Radiobiological Applications

## Slide 2
Our ambition is to:
Deliver a systematic and definitive radiation biology programme
Prove the feasibility of laser-driven hybrid acceleration
Lay the technological foundations for the transformation of PBT
  automated, patient-specific proton and ion beam therapy

## Slide 3: Radiotherapy; the challenge
Cancer: second most common cause of death globally
  Radiotherapy indicated in half of all cancer patients
Significant growth in global demand anticipated:
  14.1 million new cases in 2012 ⇢ 24.6 million by 2030
  8.2 million cancer deaths in 2012 ⇢ 13.0 million by 2030
Scale-up in provision essential:
  Projections above based on reported cases (i.e. high-income countries)
  Opportunity: save 26.9 million lives in low/middle income countries by 2035
Provision on this scale requires:
  Development of new and novel techniques … integrated in a
  Cost-effective system to allow a distributed network of RT facilities
Atun, Lancet Oncol. 2015 Sep;16(10):1153-86

## Slide 4: Particle-beam therapy
Proton and ion-beam therapy:
  Bulk of dose deposited in Bragg peak
  Significant normal-tissue sparing (entry)
  Almost no dose beyond the Bragg peak

## Slide 5: Particle beam therapy today
Cyclotron based:
  Limitations:
    Energy modulation
    Instantaneous dose rate
Synchrotron based:
  Limitiations:
    Complexity
    Instantaneous dose rate
Christie Hospital Manchester
MedAustron Austria
 reduce footprint, cost and complexity
‘PBT for the many’!
 increase flexibility
optimize treatments

## Slide 6: The case for fundamental radiobiology
Relative biological effectiveness:
  Defined relative to reference X-ray beam
  Known to depend on:
    Energy, ion species
    Dose & dose rate
    Tissue type
    Biological endpoint
Yet:
  p-treatment planning uses 1.1
  Effective values are used for C6+
Maximise the efficacy of PBT now & in the future:
  Require systematic programme to develop full understanding of radiobiology
Paganetti, van Luijk (2013)
SemRadOncol

## Slide 7: Radiobiology in new regimens
Worked example: FLASH
Conventional regime : ~2 Gy/min
FLASH regime : >40 Gy/s
Evidence of normal-tissue sparing while tumour-kill probability is maintained:
i.e. enhanced therapeutic window
Time line:
Initial reports: 2014 (e.g. Flauvadon et al, STM Jul 2014)
Confirmation in mini-pig & cat: 2018 (Clin. Cancer Research 2018)
First treatment 2019 (Bourhis et al, Rad.Onc. Oct 2019)

## Slide 8: Radiobiology in new regimens
Prezado et al
Worked example: micro beams
Conventional regime : > 1 cm diameter; homogeous
Microbeam regime : < 1 mm diameter; no dose between ‘doselets’
Remarkable increase of normal rat brain resistance.
[E.g. Dilmanian et al. 2006, Prezado et al., Rad. Research 2015]
Dose escalation in the tumour possible – larger tumor control prob.

## Slide 9: Radiobiology in new regimens
The ideally flexible beam facility can deliver it all!
 substantial opportunity for a step-change in understanding!
Time
domain
Space
domain
Energy
Ion
species
In combination and with chemo/immuno Therapies
Multidisciplinary approach essential

## Slide 11
LhARA initiative organogram

## Slide 12: Laser-hybrid Accelerator for Radiobiological Applications
A novel, hybrid, approach:
Laser-driven, high-flux proton/ion source
  Overcome instantaneous dose-rate limitation
    Capture at >10 MeV
  Delivers protons or ions in very short pulses
    Bunches as short as 10—40 ns
  Triggerable; arbitrary pulse structure
Novel “electron-plasma-lens” capture & focusing
  Strong focusing (short focal length) without the use of high-field solenoid
Fast, flexible, fixed-field post acceleration
  Variable energy
    Protons: 15—127 MeV
    Ions: 5—34 MeV/u
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 13: LhARA to serve ITRF Preliminary Activity
Preliminary Activity: £2M over 2 years
project start October 2022

## Slide 14
 compact, uniquely flexible facility
N. Bliss (DL)
Draft
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738
N. Bliss et al

## Slide 15
2-year Programme: Characterising Source and Benchmarking Simulations
J.S Green et al., NJP. 12 (2010) 085012
R. Prasad et al., Nucl. Instrum. Methods. 623.2 (2010): 712-715.
Established Diagnostics…
Established Targetry…moving toward Hz-level targetry
Typical 9-target array
Tape targetry system (online in SCAPA 2022)
….to build a systematic parameter space map of the source performance
Energy, Flux, Divergence across multiple ion species
..but also need to consider some other experimental contributions like temporal contrast
E. Boella, N. Dover, R. Gray et al

## Slide 16: LhARA Capture
“Electron-plasma” (Gabor) lens:
  Strong focusing exploiting electron gas in “Penning/Malmberg” trap
Gabor
1957
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 17: Year 5 milestone
Current
Year 2
Year 5
Final
Subsequent 3-year Programme: develop plasma parameters required for LhARA
C. Baker, W. Bertsche et al
Notes: End of 5th year milestone is to have studied plasma that have focal lengths of a few metres, comparable to many of the lens elements.
Know which 1-2 parameters need to be improved by x2 to reach final ~1m focal length lens. This is opposed to the decades improvement of many parameters needed to reach here.

## Slide 18
N. Bliss, for LhARA WP6;
ITRF 6-month progress review, 21Mar23

## Slide 19: Beam envelopes Stage 1
Propagation of “semi-realistic” source distribution:
  Generated using SMILEI
  Optimisation studies on going
HT Lau, IPAC 2021, WEPAB139
J. Pasternak, W. Shields et al

## Slide 20: Rapid, flexible acceleration for stage 2
Fixed-field alternating-gradient accelerator (FFA):
  Compact, flexible solution:
    Multiple ion species
    Variable energy extraction
    High repetition rate (rapid acceleration)
    Large acceptance
  Successfully demonstrated:
    Proof of principle at KEK
    Machines at KURNS
    Non-scaling PofP EMMA (DL)
LhARA FFA
10 cells
2 MA loaded RF cavities
Dimensions in m
bh
bv
h
J. Pasternak, W. Shields et al

## Slide 21
Opportunity; through IRC deliver our vision to:
Deliver a systematic and definitive radiation biology programme
Prove the feasibility of laser-driven hybrid acceleration
Lay the technological foundations for the transformation of PBT
  automated, patient-specific proton and ion beam therapy