## Slide 1: Laser hybrid Accelerator for Radiobiological Applications
LhARA

## Slide 2: Acknowledgements

## Slide 3: Medical accelerators; the challenge
Radiotherapy, indicated in half of all cancer patients
Significant growth in demand anticipated:
  14.1 x 106 new cases in 2012 ⇢ 24.6 x 106 by 2030
  8.2 x 106 cancer deaths in 2012 ⇢ 13.0 x 106 by 2030
Demographic:
  Projections above based on reported cases (i.e. HIC)
  Opportunity to save 26.9 x 106 lives in LMIC by 2035
Scale-up in provision:
  Requires development of new and novel techniques
Atun, Lancet Oncol. 2015 Sep;16(10):1153-86

## Slide 4: Medical accelerators; the opportunity
R&D programme:
  Incremental development of current practice
  System approach: robust, flexible next-generation facilities
  Multi-disciplinary R&D to harness novel techniques
Opportunity: contribute to underpinning science:
  Radiobiology: especially charged particle (p, ion)
  In-situ dose-deposition imaging: especially p, ion
  Integration of on-treatment imaging, simulation, planning

## Slide 5: Particle beam therapy
Proton:
  Mostly cyclotron-based
    Issues:
      Energy modulation;
      Shielding
      Source:
        Injector per ion species
        Limit to instantaneous dose rate
Proton & ion (carbon):
  Synchrotron based:
    Issues:
      Energy modulation
      Source:
        Injector per ion species
        Limit to instantaneous dose rate
Christie
MedAustron

## Slide 6: Laser-driven proton/ion source
Advantage:
  Enormous proton/ion flux at 10—15MeV in tint (30 fs) pulse
Issue to be solved:
  Efficient capture, focusing, selectin and manipulation of divergent ion beam

## Slide 7: LhARA: ion-source development
Capture
Electron plasma:
  Strong focusing of +ve ions
1st prototype:
  1 MeV protons Surrey Ion Beam Centre
  Aberrations observed
Upgraded prototype:
  Under test, Imperial
Laser source/capture test
Integration test:
  Gabor lens on Serberus Laser at Imperial
Plan:
  “Now”: validate lens with a source
  Summer: test using laser-driven source

## Slide 8: Laser-hybrid Accelerator for Radiobiological Applications
LhARA; a novel, hybrid, approach:
  High-flux, laser-driven proton/ion source;
  Novel plasma (Gabor) lens capture & focusing
  Post-acceleration and phase rotation: FFA &/or SC RF
Unique features:
  Very large flux of p or ions in very short pulses:
    Enormous instantaneous dose
  Inject at ~15 MeV into first accelerating structure
    Overcomes space-charge limit of today’s ion sources
  Staged implementation:
    In-vitro studies permitted at 15 MeV:
      Source, capture, transport
    In-vivo studies using post-accelerator (127 MeV p; ~35 MeV/u)
Uniquely flexible radiobiology facility:
  Many ions, proton to carbon, in single facility
  Wide range of energy and dose rate, allows UHDR/FLASH radiotherapy
Technologies can be developed to create uniquely flexible therapy facility
Original concept: Pozimski

## Slide 9: LhARA; stage 1
Pasternak
Capture @ 10—15 MeV
Energy selection
Phase-space matching
Vertical arc
11.6 m
Laser

## Slide 10: Conclusions
Laser-hybrid approach has potential to:
  Overcome dose-rate limitations of present PBT sources;
  Deliver uniquely flexible facility:
    Range of ion species, energy, dose, dose-rate
  Disruptive/transformative approach ‘for 2050’ …
Opportunity:
  Develop and prove novel systems in production system;
  Deliver research facility dedicated to radiobiology;
  Contribute to study of biophysics of charged-particle beams
First and next steps:
  Initial concept developed and prototype evaluation underway
  Working towards CDR for LhARA
  GSI/FAIR, this workshop, wonderful opportunity to seek synergies!