## Slide 1: The Laser-hybrid Accelerator for Radiobiological Applications LhARA
arXiv:2006.00493

## Slide 2: Acknowledgements
The LhARA consortium!
Since completion of pre-CDR (Apr20) the following groups have joined the consortium;
  The National Physical Laboratory
  Surrey
  Birmingham:
    School of Physics and Astronomy
    University Hospitals Birmingham NHS
    Foundation Trust
    Birmingham Cyclotron Facility
    Positron Imaging Centre at the University of Birmingham
  Institut Curie (Paris)
LhARA consortium Nov19

## Slide 3: Radiotherapy; the challenge
Cancer: second most common cause of death globally
  Radiotherapy indicated in half of all cancer patients
Significant growth in global demand anticipated:
  14.1 million new cases in 2012 ⇢ 24.6 million by 2030
  8.2 million cancer deaths in 2012 ⇢ 13.0 million by 2030
Scale-up in provision essential:
  Projections above based on reported cases (i.e. high-income countries)
  Opportunity: save 26.9 million lives in low/middle income countries by 2035
Provision on this scale requires:
  Development of new and novel techniques … integrated in a
  Cost-effective system to allow a distributed network of RT facilities
Atun, Lancet Oncol. 2015 Sep;16(10):1153-86

## Slide 4: Particle-beam therapy
Proton and ion-beam therapy:
  Bulk of dose deposited in Bragg peak
  Significant normal-tissue sparing (entry)
  Almost no dose beyond the Bragg peak

## Slide 5: LhARA … the vision
The execution of the LhARA programme will:
Create the capability to deliver particle-beam therapy in completely new regimes
  by combining a variety of ion species in a single treatment fraction and exploiting ultra-high dose rates and novel spatial-fractionation schemes.
Make "best in class" treatments available to the many
  by demonstrating in operation a system that incorporates dose-deposition imaging in a fast feedback-and-control system thereby reducing the requirement for a large gantry.

## Slide 6: The radiobiology needs to be understood
Treatment planning:
  Based on ‘Relative Biological Effectiveness (RBE)
    Proton-treatment planning uses RBE = 1.1
    Effective values are used for C6+
Paganetti, van Luijk Sem. Rad. Oncol (2013)
Essential: improved, fundamental, understanding of radiobiology
RBE:
Ratio of dose required to gain same biological response as reference photon beam
RBE known to depend on:
Energy, ion species
Dose & dose rate
Tissue type
Biological endpoint

## Slide 7: Radiobiology in new regimens
The ideally flexible beam facility can deliver it all!
 substantial opportunity for a step-change in understanding!
Time
domain
Space
domain
Energy
Ion
species
In combination and with chemo/immuno Therapies

## Slide 8: Laser-hybrid Accelerator for Radiobiological Applications
LhARA; a novel, hybrid, approach:
High-flux, laser-driven proton/ion source:
  Overcome instantaneous dose-rate limitation
  Delivers protons or ions in very short pulses:
    Pulse length 10 – 40 ns
  Can provide arbitrary pulse structure
Novel plasma-lens capture & focusing
Fast, flexible, fixed-field post acceleration
  Protons up to 127 MeV p;
  Ions up to ~35 MeV/u
Staged implementation:
  Stage 1: In vitro studies with protons at energies up to 15 MeV
  Stage 2: In vivo & in vitro studies with protons up to 127 MeV and ions up to 33 MeV/u
→ compact, uniquely flexible facility
LhARA consortium
arXiv:2006.00493

## Slide 9: Sheath acceleration
Laser incident on foil target:
  Drives electrons from material
  Creates enormous electric field
Field accelerates protons/ions
  Dependent on nature of target
First observation ~2000
Active development:
  Laser: power and rep. rate
  Target material, transport
Schwoerer, H. et al., 2006; Nature, 439(7075).

## Slide 10
LhARA
arXiv:2006.00493

## Slide 11: LhARA: ion-source development
Capture
Electron plasma:
  Strong focusing of +ve ions
1st prototype:
  1 MeV protons Surrey Ion Beam Centre
  Aberrations observed
Upgraded prototype:
  Under development Imperial
Laser source/capture test
Integration test:
  Gabor lens on cerberus Laser at Imperial
Plan:
  “Now”: prepare to validate lens with a
  Next: test using laser-driven source

## Slide 12: LhARA; stage 1
Pasternak
arXiv:2006.00493

## Slide 13: LhARA – Stage 2
In-vitro radiobiology using animal models:
  Post-acceleration required
Baseline: fixed field accelerator:
  x3 increase in momentum
    15 MeV protons accelerated to 127 MeV
    3.8 MeV/u carbon 6+ ions accelerated to 33 MeV/u
arXiv:2006.00493

## Slide 14: Next steps; 5-year R&D plan
5-year plan presented in pre-CDR designed to:
  Address technical risks presented in pre-CDR
    Especially source and plasma-lens capture
    Instrumentation and diagnostics
  Deliver technical designs for the LhARA facility
  End stations.
    Automation, sample handling, imaging
    Simulation, including impact on tissue/tissue response
→ Capability to start Stage 1 in-vitro programme
arXiv:2006.00493

## Slide 15: Conclusions
Laser-hybrid approach has potential to:
  Overcome dose-rate limitations of present PBT sources;
  Deliver uniquely flexible facility:
    Range of ion species, energy, dose, dose-rate
  Disruptive/transformative approach ‘for 2050’ …
Opportunity:
  Develop and prove novel systems in production system;
  Deliver research facility dedicated to radiobiology;
  Contribute to study of biophysics of charged-particle beams
First and next steps:
  Initial concept developed and prototype evaluation underway
  Seeking resources to execute R&D programme laid out in ‘pre-CDR’
  Wonderful opportunity to build novel techniques to spin back in!
K.Long@imperial.ac.uk

## Slide 16: Backup
Laser-hybrid Accelerator for Radiobiological Applications (LhARA)

## Slide 17: LhARA status
Modest resources to date have delivered LhARA "pre-CDR":
STFC Opportunities 2019 award; and consortium
Milestone: pre-CDR by April 2020:
Completed.
  Review by international panel 25&31 Mar20
    Peer-endorsement subsequent to 2019 PPRP review
Publication based on the pre-CDR:
  Submitted to Frontiers in Physics Medical Physics and Imaging
  Uploaded to the arXiv as arXiv:2006.00493