## Slide 1: The Laser-hybrid Accelerator for Radiobiological Applications LhARA
arXiv:2006.00493

## Slide 2: Challenges and opportunities
The Laser-hybrid Accelerator for Radiobiological Applications (LhARA)

## Slide 3: Radiotherapy; the challenge
Cancer is the second leading cause of death globally (WHO)
  Radiotherapy indicated in half of all cancer patients
Growing requirement for radiotherapy:
  High-income countries: anticipate significant growth in demand
  Low/middle income countries; enormous unmet need:
    Opportunity to save ~30 million lives by 2035
Scale-up in provision essential:
  Requires:
    Development of new and novel techniques … integrated in a
    Cost-effective system to allow a distributed network of RT facilities
Atun, Lancet Oncol. 2015 Sep;16(10):1153-86

## Slide 4: Particle-beam therapy
Proton and ion-beam therapy:
  Bulk of dose deposited in Bragg peak
  Significant normal-tissue sparing (entry)
  Almost no dose beyond the Bragg peak

## Slide 5: LhARA … the vision
The execution of the LhARA programme will:
Create the capability to deliver particle-beam therapy in completely new regimens
  Flexibility!
    Combine a variety of ion species in a single treatment fraction, exploiting ultra-high dose rates in novel spatial- and spectral-fractionation schemes
Make "best in class" treatments available to the many
  Automated, triggerable system → reduce requirement for large gantry:
    System incorporating dose-deposition imaging in fast feedback-and-control system; track movement, deliver dose at optimum tissue alignment

## Slide 6: Radiobiology
The Laser-hybrid Accelerator for Radiobiological Applications (LhARA)

## Slide 7: The radiobiology needs to be understood
Treatment planning:
  Based on RBE:
    Proton-treatment planning uses RBE = 1.1
    Effective values are used for C6+
Paganetti, van Luijk Sem. Rad. Oncol (2013)
Essential: improved, fundamental, understanding of radiobiology
Relative Biological Effectivness (RBE):
Ratio of dose required to gain same biological response as reference photon beam
RBE known to depend on:
Energy, ion species
Dose & dose rate
Tissue type
Biological endpoint

## Slide 8: Biological impact from the physics of ionisation
Low-LET radiation:
  Repairable single/double strand breaks
High-LET radiation:
  Complex DNA lesions
    Multiple DNA pathways
    More difficult to repair
    Enhances cell death
Programmatic approach:
  Dynamic studies of impact of radiation
  Interpret with advanced computer models (e.g. G4DNA)
Parsons et al.

## Slide 9: Radiobiology in new regimens
Worked example: FLASH
Conventional regime n: ~2 Gy/min
FLASH regime : >40 Gy/s
Evidence of normal-tissue sparing while tumour-kill probability is maintained:
i.e. enhanced therapeutic window
Time line:
Initial reports: 2014 (e.g. Flauvadon et al, STM Jul 2014)
Confirmation in mini-pig & cat: 2018 (Clin. Cancer Research 2018)
First treatment 2019 (Bourhis et al, Rad.Onc. Oct 2019)
Temporal dependence

## Slide 10: Radiobiology in new regimens
Worked example: micro beams
Conventional regime : > 1 cm diameter; homogeous
Microbeam regime : < 1 mm diameter; no dose between ‘doselets’
Remarkable increase of normal rat brain resistance.
[Dilmanian et al. 2006, Prezado et al., Rad. Research 2015]
Dose escalation in the tumour possible – larger tumor control prob.
Spatial dependence

## Slide 11: Radiobiology in new regimens

## Slide 12: LhARA
The Laser-hybrid Accelerator for Radiobiological Applications (LhARA)

## Slide 13: Laser-hybrid Accelerator for Radiobiological Applications
A novel, hybrid, approach:
Laser-driven, high-flux proton/ion source
  Overcome instantaneous dose-rate limitation
    Capture at >10 MeV
  Delivers protons or ions in very short pulses
    Bunches as short as 10—40 ns
  Triggerable; arbitrary pulse structure
Novel “electron-plasma-lens” capture & focusing
  Strong focusing (short focal length) without the use of high-field solenoid
Fast, flexible, fixed-field post acceleration
  Variable energy
    Protons: 15—127 MeV
    Ions: 5—34 MeV/u

## Slide 14
LhARA
arXiv:2006.00493

## Slide 15: Sheath acceleration
Laser incident on foil target:
  Drives electrons from material
  Creates enormous electric field
Field accelerates protons/ions
  Dependent on nature of target
Active development:
  Laser: power and rep. rate
  Target material, transport
Schwoerer, H. et al., 2006; Nature, 439(7075).

## Slide 16: Beam capture/production principle
“Electron-plasma” (Gabor) lens:
  Strong focusing exploiting electron gas in “Penning/Malmberg” trap
Posocco, Pozimski
Gabor
1957
arXiv:2006.00493

## Slide 17: Energy collimation
Flat initial energy profile
3 collimators
  Energy collimation (at beam focus, controls energy spread)
  Beam shaping
  Momentum cleaning (removes energy tails)
1
2
3
LhARA Stage 1 beamline

## Slide 18: LhARA; stage 1
Pasternak
arXiv:2006.00493
arXiv:2006.00493
Dose uniformity at end station

## Slide 19: Rapid, flexible acceleration for stage 2
Fixed-field alternating-gradient accelerator (FFA):
  Invented in 1950s
    Kolomensky, Okhawa, Symon
  Compact, flexible solution:
    Multiple ion species
    Variable energy extraction
    High repetition rate (rapid acceleration)
    Large acceptance
  Successfully demonstrated:
    Proof of principle at KEK
    Machines at KURNS
    Non-scaling pop, EMMA, at DL
LhARA FFA
10 cells
2 MA loaded RF cavities
Dimensions in m
arXiv:2006.00493
Evolution of RACCAM design; prototype magnet demonstrated
bh
bv
h

## Slide 20: FFA for acceleration in LhARA – Stage 2
Baseline: x3 increase in momentum
  15 MeV protons accelerated to 127 MeV
  3.8 MeV/u carbon 6+ ions accelerated to 34 MeV/u
arXiv:2006.00493

## Slide 21: LhARA performance: doses and dose rates

## Slide 22: Conclusions
The Laser-hybrid Accelerator for Radiobiological Applications (LhARA)

## Slide 23: Conclusions
LhARA consortium has:
  Developed the concept of a laser-hybrid accelerator for biomedical applications
Laser-hybrid approach has potential to:
  Overcome dose-rate limitations of present PBT sources
  Deliver uniquely flexible facility:
    Range of: ion species; energy; dose; dose-rate; time; and spatial distribution
  Be used in automated, triggerable system → reduce requirement for large gantry
    Disruptive/transformative approach to “distributed PBT for 2050”
The LhARA consortium now seeks the opportunity to:
  Prove the novel laser-hybrid systems in operation
  Contribute to the study of the biophysics of charged-particle beams
    Enhance treatment planning
  Create novel capabilities to ‘spin back in’ to science and innovation

## Slide 24: Acknowledgements
The LhARA consortium