## Slide 1: The Laser-hybrid Accelerator for Radiobiological Applications LhARA
a step on the route to precision particle-beam therapy

## Slide 2: Challenges and opportunities
Perspectives on laser-driven sources for particle beam therapy

## Slide 3: Radiotherapy; the challenge
Cancer: second most common cause of death globally
  Radiotherapy indicated in half of all cancer patients
Significant growth in global demand anticipated:
  14.1 million new cases in 2012 ⇢ 24.6 million by 2030
  8.2 million cancer deaths in 2012 ⇢ 13.0 million by 2030
Scale-up in provision essential:
  Projections above based on reported cases (i.e. high-income countries)
  Opportunity: save 26.9 million lives in low/middle income countries by 2035
Provision on this scale requires:
  Development of new and novel techniques … integrated in a
  Cost-effective system to allow a distributed network of RT facilities
Atun, Lancet Oncol. 2015 Sep;16(10):1153-86

## Slide 4: The benefit of particles
Maximise therapeutic benefit by:
  Maximising damage to tumour
  Minimising damage to healthy tissue
X-ray therapy:
  Modality used in most radiotherapy
  Dose falls exponentially with depth
  Proximity of sensitive organs limits dose to tumour

## Slide 5: Particle-beam therapy
Proton and ion-beam therapy:
  Bulk of dose deposited in Bragg peak
  Significant normal-tissue sparing (entry)
  Almost no dose beyond the Bragg peak

## Slide 6: The need for a step-change in capability
Growing recognition of benefits of PBT worldwide:
  70 PBT centres in operation; 40 under construction
‘Incremental’ development of technique
  Existing suppliers
  New initiatives
Exciting indications of benefits of novel beams …

## Slide 7: Particle beam therapy today
Cyclotron based
Synchrotron based
Christie Hospital Manchester
MedAustron Austria

## Slide 8: Beam delivery
PSI gantry
  Engineering tour de force!
  360-degree irradiation
  At a price: Size, complexity, maintenance
H. Owen
PSI gantry

## Slide 9: Particle source
Extraction energy:
  30—80 keV
    Limited by extraction voltage
Instantaneous flux (current or dose):
  Determined by acceptance of first accelerator structure
    Limited by mutual repulsion of protons (ions) … “space-charge effect”
S. Laurie
S. Laurie

## Slide 10: The technological challenge
Cancer is the second leading cause of death globally (WHO)
  Radiotherapy indicated in half of all cancer patients
Growing requirement for radiotherapy:
  High-income countries: anticipate significant growth in demand
  Low/middle income countries; enormous unmet need:
    Opportunity to save ~30 million lives by 2035
Scale-up in provision essential:
  Requires:
    Development of new and novel techniques … integrated in a
    Cost-effective system to allow a distributed network of RT facilities
Atun, Lancet Oncol. 2015 Sep;16(10):1153-86

## Slide 11: Radiobiology
The Laser-hybrid Accelerator for Radiobiological Applications (LhARA)

## Slide 13: The case for fundamental radiobiology
Relative biological effectiveness:
  Defined relative to reference X-ray beam
  Known to depend on:
    Energy, ion species
    Dose & dose rate
    Tissue type
    Biological endpoint
Yet:
  p-treatment planning uses 1.1
  Effective values are used for C6+
Maximise the efficacy of PBT now & in the future:
  Require systematic programme to develop full understanding of radiobiology
Paganetti, van Luijk (2013)
SemRadOncol

## Slide 14: Biological impact from the physics of ionisation
Low-LET radiation:
  Repairable single/double strand breaks
High-LET radiation:
  Complex DNA lesions
    Multiple DNA pathways
    More difficult to repair
    Enhances cell death
Programmatic approach:
  Dynamic studies of impact of radiation
  Interpret with advanced computer models (e.g. G4DNA)

## Slide 15: A complex, multi-facetted problem
Time
Carter et al, and Parsons (2018) IJROBP & (2019) IJROBP

## Slide 16: Radiobiology in new regimens
Worked example: FLASH
Conventional regime : ~2 Gy/min
FLASH regime : >40 Gy/s
Evidence of normal-tissue sparing while tumour-kill probability is maintained:
i.e. enhanced therapeutic window
Time line:
Initial reports: 2014 (e.g. Flauvadon et al, STM Jul 2014)
Confirmation in mini-pig & cat: 2018 (Clin. Cancer Research 2018)
First treatment 2019 (Bourhis et al, Rad.Onc. Oct 2019)

## Slide 17: Radiobiology in new regimens
Prezado; 13Nov19
Worked example: micro beams
Conventional regime : > 1 cm diameter; homogeous
Microbeam regime : < 1 mm diameter; no dose between ‘doselets’
Remarkable increase of normal rat brain resistance.
[Dilmanian et al. 2006, Prezado et al., Rad. Research 2015]
Dose escalation in the tumour possible – larger tumor control prob.

## Slide 18: Radiobiology in new regimens
The ideally flexible beam facility can deliver it all!
 substantial opportunity for a step-change in understanding!
Time
domain
Space
domain
Energy
Ion
species
In combination and with chemo/immuno Therapies
Multidisciplinary approach essential

## Slide 20: Laser-driven sources are disruptive
I will argue that laser-driven sources have the potential to:
Create the capability to deliver particle-beam therapy in completely new regimens
  Flexibility!
    Combine a variety of ion species in a single treatment fraction, exploiting ultra-high dose rates in novel spatial- and spectral-fractionation schemes
Make "best in class" treatments available to the many
  Automated, triggerable system → remove requirement for large gantry:
    System incorporating dose-deposition imaging in fast feedback-and-control system; track movement, deliver dose at optimum tissue alignment

## Slide 21: The in-principle advantage of the laser-driven source
Perspectives on laser-driven sources for particle beam therapy

## Slide 22: Sheath acceleration
Laser incident on foil target:
  Drives electrons from material
  Creates enormous electric field
Field accelerates protons/ions
  Dependent on nature of target
Active development:
  Laser: power and rep. rate
  Target material, transport
Schwoerer, H. et al., 2006; Nature, 439(7075).

## Slide 23: Advances
Ultrathin foil irradiated by "long", linearly-polarised laser pulse
Mechanism:
  Radiation-pressure/target-normal sheath acceleration
  High-energies confined to narrow angular range by radiation-induced transparency
(2018)9:724 DOI: 10.1038/s41467-018-03063-9
Vulcan
Production: 63Cu(p,n)63Zn
63Zn – b+decay

## Slide 24: Advantages
Protons (and ions) produced at “high energy”:
  e.g. 15 MeV  250 times energy of conventional proton source
    High energy substantially reduced impact of space charge
      Allows evasion of instantaneous dose-rate limitation of today’s sources
Pulsed operation “natural”:
  Discharge sources are DC; accelerator imposes time structure
  Pulsed operation determined by laser:
    A triggerable, “on demand”, source
Critical issues:
  Efficient capture of divergent, high-energy ion flux
  Transformation of captured flux into useful beam

## Slide 25: ELIMAIA-ELIMED
Extreme Light Infrastructure, Prague, Czech Republic:
ELI Multidisciplinary Applications of laser-Ion Acceleration (ELIMAIA)
  ELI MEDical and multidisciplinary applications (ELIMED)
    ELIMAIA section dedicated to ion focusing, selection, characterization, and irradiation
  Proton energies from 5 to 250 MeV transported to in-air section
Quantum Beam Sci. 2018, 2, 8; doi:10.3390/qubs2020008
Frontiers in Phys. Med. Phys. & Imag. – doi: 10.3389/fphy.2020.564907

## Slide 26: Many initiatives in Americas, Europe, Asia
Applications in biological research, ambition to push toward clinical application …
  Phys Lett A. (2002) 299:240–7. doi: 10.1016/S0375-9601(02)00521-2
  Med Phys. (2003) 30:1660–70. doi: 10.1118/1.1586268
  Med Phys. (2004) 31:1587–92. doi: 10.1118/1.1747751
  Science. (2003) 300:1107–111
  New J Phys. (2010) 12:85003. doi: 10.1088/1367-2630/12/8/085003
  Phys Med Biol. (2011) 56:6969–82. doi: 10.1088/0031-9155/56/21/013
  Appl Phys Lett. (2011) 98:053701. doi: 10.1063/1.3551623
  Appl Phys Lett. (2012) 101:243701. doi: 10.1063/1.4769372
  AIP Adv. (2012) 2:011209. doi: 10.1063/1.3699063
  Appl Phys B. (2013) 110:437–44. doi: 10.1007/s00340-012-5275-3
  Appl Phys B. (2014) 117:41–52. doi: 10.1007/s00340-014-5796-z
  Radiat Res. (2014) 181:177–83. doi: 10.1667/RR13464.1
  Phys Rev Acceler Beams. (2017) 20:1–10. doi: 10.1103/PhysRevAccelBeams.20.032801
  J Instrum. (2017) 12:C03084. doi: 10.1088/1748-0221/12/03/C03084
  A-SAIL Project. (2020). Available online at: https://www.qub.ac.uk/research-centres/A-SAILProject/
  Vol. 8779. Prague: International Society for Optics and Photonics. SPIE (2013). p. 216–25.
  Vol. 11036. International Society for Optics and Photonics. SPIE (2019). p. 93–103.
  Nuovo Cim C. (2020) 43:15. doi: 10.1393/ncc/i2020-20015-6
  10th International Particle Accelerator Conference. Melbourne, VIC (2019). p. TUPTS005.
I will not attempt a review, choosing instead to focus on opportunity …
A selection …

## Slide 27: Opportunity; a hybrid approach
Create protons (ions) at “modest” energy:
  Consider 10—15 MeV; high flux, “plateau” region
Capture and manipulate proton (ion) flux:
  Inject into post accelerator for biomedical application
High Energy Density Physics 37 (2020) 100847

## Slide 28: Laser-hybrid Accelerator for Radiobiological Applicatons
Vision:
LhARA will be a uniquely-flexible, novel system that will:
Deliver a systematic and definitive radiobiology programme
Prove the feasibility of the laser-driven hybrid-accelerator approach
Lay the technological foundations for the transformation of PBT
  automated, patient-specific: implies online imaging & fast feedback and control
Ambition:
  Develop:
    necessary techniques, technologies, and systems
  Exploit:
    system approach to novel bring techniques into clinical practice as they mature
  Integrate:
    production prototypes in a production system for radiobiological research
  Engage:
    industry and clinical PBT centres
    during development of techniques, technologies, and systems

## Slide 29: LhARA
Perspectives on laser-driven sources for particle beam therapy

## Slide 30: Laser-hybrid Accelerator for Radiobiological Applications
A novel, hybrid, approach:
Laser-driven, high-flux proton/ion source
  Overcome instantaneous dose-rate limitation
    Capture at >10 MeV
  Delivers protons or ions in very short pulses
    Bunches as short as 10—40 ns
  Triggerable; arbitrary pulse structure
Novel “electron-plasma-lens” capture & focusing
  Strong focusing (short focal length) without the use of high-field solenoid
Fast, flexible, fixed-field post acceleration
  Variable energy
    Protons: 15—127 MeV
    Ions: 5—34 MeV/u
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 31
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 32: Laser-driven proton/ion source
Advantage:
  Enormous proton/ion flux at 10—15MeV in tiny (30 fs) pulse at 10 Hz
Requirement:
  Efficient capture, focusing, selection and manipulation of divergent ion beam
Ti:Sapphire commercial system >15TW
Pulse ~35fs at rep-rate of at least 10Hz
At least 500mJ laser energy - IL ~ 1020 Wcm-2
HT Lau

## Slide 33: Beam capture/production principle
“Electron-plasma” (Gabor) lens:
  Strong focusing exploiting electron gas in “Penning/Malmberg” trap
Posocco, Pozimski
Gabor
1957
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 34
VSIM/BDSIM:
evaluation of m = 1
diocotron mode
Dascalu

## Slide 35: Energy collimation
Flat initial energy profile
3 collimators
  Energy collimation (at beam focus, controls energy spread)
  Beam shaping
  Momentum cleaning (removes energy tails)
1
2
3
LhARA Stage 1 beamline

## Slide 37: LhARA; stage 1
Pasternak
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738
Dose uniformity at end station
HT Lau

## Slide 38: LhARA – Stage 2
In-vitro radiobiology using animal models:
  Post-acceleration required
Baseline:fixed field accelerator:
  x3 increase in momentum
    15 MeV protons accelerated to 127 MeV
    3.8 MeV/u carbon 6+ ions accelerated to 33 MeV/u

## Slide 39: Fixed Field Accelerator
Advantages over conventional medical cyclotron
  Variable energy operation without energy degraders
  Operation with different ions
  Multiple extraction ports
Bending magnetic fields do not vary in time.
  Rapid acceleration.
Alternating gradient gives strong focussing.
Very large acceptance.
  Useful, e.g. to accelerate muon beams.

## Slide 40: FFA potted history
Early 1950s, FFAG developed independently:
  Japan by Tihiro Ohkawa
  US by Keith Symon
  Russia by Andrei Kolomensky.
The first prototype was operated in 1956
  Jones, Terwilliger, Technical Report MURA-LWJ/KMT-5 (MURA-104), April 3, 1956.
Not much activity until first proton accelerator in 2000
PRISM muon beam phase rotation demonstration ring at Osaka.
The Michigan Mark I FFA 400KeV electron accelerator was the first operational FFA.
EMMA at Daresbury
500 keV Proton proof-of-principle FFA at KEK.
Kyoto University FFA for ADSR

## Slide 41: Rapid, flexible acceleration for stage 2
Fixed-field alternating-gradient accelerator (FFA):
  Invented in 1950s
    Kolomensky, Okhawa, Symon
  Compact, flexible solution:
    Multiple ion species
    Variable energy extraction
    High repetition rate (rapid acceleration)
    Large acceptance
  Successfully demonstrated:
    Proof of principle at KEK
    Machines at KURNS
    Non-scaling pop, EMMA, at DL
LhARA FFA
10 cells
2 MA loaded RF cavities
Dimensions in m
Evolution of RACCAM design; prototype magnet demonstrated
bh
bv
h
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 42: FFA for acceleration in LhARA – Stage 2
Baseline: x3 increase in momentum
  15 MeV protons accelerated to 127 MeV
  3.8 MeV/u carbon 6+ ions accelerated to 34 MeV/u
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 43: LhARA performance: doses and dose rates
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 44: Conclusions
Perspectives on laser-driven sources for particle beam therapy

## Slide 45
2040
2050
1970
1980
1990
2000
2010
2020
2030
1946
↓
1960
Novel accelerator techniques
System: image processing
fast feedback, control
Fundamental
biology & biochemistry

## Slide 46
Novel accelerator techniques
System: image processing
fast feedback, control
Fundamental
Biology & biochemistry

## Slide 47: Conclusions
Laser-driven sources are disruptive technologies …
  With the potential to drive a step-change in clinical capability
Laser-hybrid approach has potential to:
  Overcome dose-rate limitations of present PBT sources
  Deliver uniquely flexible facility:
    Range of: ion species; energy; dose; dose-rate; time; and spatial distribution
  Be used in automated, triggerable system → reduce requirement for large gantry
    Disruptive/transformative approach to “distributed PBT for 2050”
The LhARA collaboration now seeks to:
  Prove the novel laser-hybrid systems in operation
  Contribute to the study of the biophysics of charged-particle beams
    Enhance treatment planning
  Create novel capabilities to ‘spin back in’ to science and innovation

## Slide 48: Acknowledgements