## Slide 1: Proton & ion beams for bio-medical application; the next generation
a step on the route to precision particle-beam therapy

## Slide 2: opportunity
Proton & ion beams for bio-medical application; the next generation

## Slide 3: Radiotherapy; the challenge
Cancer: second most common cause of death globally
  Radiotherapy indicated in half of all cancer patients
Significant growth in global demand anticipated:
  14.1 million new cases in 2012 ⇢ 24.6 million by 2030
  8.2 million cancer deaths in 2012 ⇢ 13.0 million by 2030
Scale-up in provision essential:
  Projections above based on reported cases (i.e. high-income countries)
  Opportunity: save 26.9 million lives in low/middle income countries by 2035
Provision on this scale requires:
  Development of new and novel techniques … integrated in a
  Cost-effective system to allow a distributed network of RT facilities
Atun, Lancet Oncol. 2015 Sep;16(10):1153-86

## Slide 4: The benefit of particles
Maximise therapeutic benefit by:
  Maximising damage to tumour
  Minimising damage to healthy tissue
X-ray therapy:
  Modality used in most radiotherapy
  Dose falls exponentially with depth
  Proximity of sensitive organs limits dose to tumour

## Slide 5: Particle-beam therapy
Proton and ion-beam therapy:
  Bulk of dose deposited in Bragg peak
  Significant normal-tissue sparing (entry)
  Almost no dose beyond the Bragg peak

## Slide 6: Disruptive technology
Proton & ion beams for bio-medical application; the next generation

## Slide 7: Protons for clinical use
First proposed by R. R. Wilson
  “Radiological Use of Fast Protons” R.R. Wilson Radiology 47:487-491, 1946.
Treatment started in 1954 at LBNL
  “Pituitary irradiation with high-energy proton beams: a preliminary report.” C. A. Tobias et al. Cancer Res. 18(2):121-34, 1958

## Slide 8: Particle beam therapy today
Cyclotron based
Synchrotron based
Christie Hospital Manchester
MedAustron Austria

## Slide 9: Beam delivery
PSI gantry
  Engineering tour de force!
  360-degree irradiation
  At a price: Size, complexity, maintenance
H. Owen
PSI gantry

## Slide 10: Particle source
Extraction energy:
  Low
Instantaneous dose:
  Limited at source
S. Laurie
S. Laurie

## Slide 11: Radiobiology
Proton & ion beams for bio-medical application; the next generation

## Slide 12: Biological impact from the physics of ionisation
Low-LET radiation:
  Repairable single/double strand breaks
High-LET radiation:
  Complex DNA lesions
    Multiple DNA pathways
    More difficult to repair
    Enhances cell death
Programmatic approach:
  Systematic studies of impact of radiation

## Slide 13: The case for fundamental radiobiology
Relative biological effectiveness:
  Defined relative to reference X-ray beam
  Known to depend on:
    Energy, ion species
    Dose & dose rate
    Tissue type
    Biological endpoint
Yet:
  p-treatment planning uses 1.1
  Effective values are used for C6+
Maximise the efficacy of PBT:
  Require full understanding of radiobiology
Paganetti, van Luijk (2013)
SemRadOncol

## Slide 14: Radiobiology in new regimens
The ideally flexible beam facility can deliver it all!
 substantial opportunity for a step-change in understanding!
Time
domain
Space
domain
Energy
Ion
species
In combination and with chemo/immuno Therapies
Multidisciplinary approach essential

## Slide 16: Disruptive technology
Proton & ion beams for bio-medical application; the next generation

## Slide 17: Sheath acceleration
Laser incident on foil target:
  Drives electrons from material
  Creates enormous electric field
Field accelerates protons/ions
  Dependent on nature of target
Active development:
  Laser: power and rep. rate
  Target material, transport
Schwoerer, H. et al., 2006; Nature, 439(7075).

## Slide 18: Advances
Ultrathin foil irradiated by "long", linearly-polarised laser pulse
Mechanism:
  Radiation-pressure/target-normal sheath acceleration
  High-energies confined to narrow angular range by radiation-induced transparency
(2018)9:724 DOI: 10.1038/s41467-018-03063-9
Vulcan
Production: 63Cu(p,n)63Zn
63Zn – b+decay

## Slide 19: Advantages
Protons (and ions) produced at “high energy”:
  e.g. 15 MeV  250 times energy of conventional proton source
    High energy substantially reduced impact of space charge
      Allows evasion of instantaneous dose-rate limitation of today’s sources
Pulsed operation “natural”:
  Discharge sources are DC; accelerator imposes time structure
  Pulsed operation determined by laser:
    A triggerable, “on demand”, source
Critical issues:
  Efficient capture of divergent, high-energy ion flux
  Transformation of captured flux into useful beam

## Slide 20: LhARA
Proton & ion beams for bio-medical application; the next generation

## Slide 21: Laser-hybrid Accelerator for Radiobiological Applications
A novel, hybrid, approach:
Laser-driven, high-flux proton/ion source
Novel “electron-plasma-lens” capture & focusing
Fast, flexible, fixed-field post acceleration
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 22
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 23: Laser-driven proton/ion source
Advantage:
  Enormous proton/ion flux at 10—15MeV in tiny (30 fs) pulse at 10 Hz
Requirement:
  Efficient capture, focusing, selection and manipulation of divergent ion beam
Ti:Sapphire commercial system >15TW
Pulse ~35fs at rep-rate of at least 10Hz
At least 500mJ laser energy - IL ~ 1020 Wcm-2
HT Lau

## Slide 24: Beam capture/production principle
“Electron-plasma” (Gabor) lens:
  Strong focusing exploiting electron gas in “Penning/Malmberg” trap
Posocco, Pozimski
Gabor
1957
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 26: Rapid, flexible acceleration for stage 2
Fixed-field alternating-gradient accelerator (FFA):
  Invented in 1950s
    Kolomensky, Okhawa, Symon
  Compact, flexible solution:
    Multiple ion species
    Variable energy extraction
    High repetition rate (rapid acceleration)
    Large acceptance
  Successfully demonstrated:
    Proof of principle at KEK
    Machines at KURNS
    Non-scaling pop, EMMA, at DL
LhARA FFA
10 cells
2 MA loaded RF cavities
Dimensions in m
Evolution of RACCAM design; prototype magnet demonstrated
bh
bv
h
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 27: LhARA performance: doses and dose rates
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 28: Conclusions
Proton & ion beams for bio-medical application; the next generation

## Slide 29: Conclusions
Laser-driven sources are disruptive technologies …
  With the potential to drive a step-change in clinical capability
Laser-hybrid approach has potential to:
  Overcome dose-rate limitations of present PBT sources
  Deliver uniquely flexible facility:
    Range of: ion species; energy; dose; dose-rate; time; and spatial distribution
  Be used in automated, triggerable system → reduce requirement for large gantry
    Disruptive/transformative approach to “distributed PBT for 2050”
The LhARA collaboration now seeks to:
  Prove the novel laser-hybrid systems in operation
  Contribute to the study of the biophysics of charged-particle beams
    Enhance treatment planning
  Create novel capabilities to ‘spin back in’ to science and innovation