## Slide 1: The Laser-hybrid Accelerator for Radiobiological Applications LhARA
arXiv:2006.00493

## Slide 2: Acknowledgements
The LhARA consortium
To be updated!

## Slide 3: Challenges and opportunities
The Laser-hybrid Accelerator for Radiobiological Applications (LhARA)

## Slide 4: Radiotherapy; the challenge
Cancer: second most common cause of death globally
  Radiotherapy indicated in half of all cancer patients
Significant growth in global demand anticipated:
  14.1 million new cases in 2012 ⇢ 24.6 million by 2030
  8.2 million cancer deaths in 2012 ⇢ 13.0 million by 2030
Scale-up in provision essential:
  Projections above based on reported cases (i.e. high-income countries)
  Opportunity: save 26.9 million lives in low/middle income countries by 2035
Provision on this scale requires:
  Development of new and novel techniques … integrated in a
  Cost-effective system to allow a distributed network of RT facilities
Atun, Lancet Oncol. 2015 Sep;16(10):1153-86

## Slide 5: The benefit of particles
Maximise therapeutic benefit by:
  Maximising damage to tumour
  Minimising damage to healthy tissue
X-ray therapy:
  Modality used in most radiotherapy
  Dose falls exponentially with depth
  Proximity of sensitive organs limits dose to tumour

## Slide 6: Particle-beam therapy
Proton and ion-beam therapy:
  Bulk of dose deposited in Bragg peak
  Significant normal-tissue sparing (entry)
  Almost no dose beyond the Bragg peak

## Slide 7: The need for a step-change in capability
Growing recognition of benefits of PBT worldwide:
  70 PBT centres in operation; 40 under construction
‘Incremental’ development of technique
  Existing suppliers
  New initiatives
Exciting indications of benefits of novel beams …

## Slide 8: LhARA … the vision
The execution of the LhARA programme will:
Create the capability to deliver particle-beam therapy in completely new regimes
  by combining a variety of ion species in a single treatment fraction and exploiting ultra-high dose rates and novel spatial-fractionation schemes.
Make "best in class" treatments available to the many
  by demonstrating in operation a system that incorporates dose-deposition imaging in a fast feedback-and-control system thereby reducing the requirement for a large gantry.

## Slide 9: Radiobiology
The Laser-hybrid Accelerator for Radiobiological Applications (LhARA)

## Slide 10: The radiobiology needs to be understood
Treatment planning:
  Based on ‘Relative Biological Effectiveness (RBE)
    Proton-treatment planning uses RBE = 1.1
    Effective values are used for C6+
Paganetti, van Luijk Sem. Rad. Oncol (2013)
Essential: improved, fundamental, understanding of radiobiology
RBE:
Ratio of dose required to gain same biological response as reference photon beam
RBE known to depend on:
Energy, ion species
Dose & dose rate
Tissue type
Biological endpoint

## Slide 11: Biological impact from the physics of ionisation
Low-LET radiation:
  Repairable single/double strand breaks
High-LET radiation:
  Complex DNA lesions
    Multiple DNA pathways
    More difficult to repair
    Enhances cell death
Programmatic approach:
  Dynamic studies of impact of radiation
  Interpret with advanced computer models (e.g. G4DNA)

## Slide 12: Radiobiology in new regimens
Worked example: FLASH
Conventional regime : ~2 Gy/min
FLASH regime : >40 Gy/s
Evidence of normal-tissue sparing while tumour-kill probability is maintained:
i.e. enhanced therapeutic window
Time line:
Initial reports: 2014 (e.g. Flauvadon et al, STM Jul 2014)
Confirmation in mini-pig & cat: 2018 (Clin. Cancer Research 2018)
First treatment 2019 (Bourhis et al, Rad.Onc. Oct 2019)

## Slide 13: Radiobiology in new regimens
Prezado; 13Nov19
Worked example: micro beams
Conventional regime : > 1 cm diameter; homogeous
Microbeam regime : < 1 mm diameter; no dose between ‘doselets’
Remarkable increase of normal rat brain resistance.
[Dilmanian et al. 2006, Prezado et al., Rad. Research 2015]
Dose escalation in the tumour possible – larger tumor control prob.

## Slide 14: Radiobiology in new regimens
The ideally flexible beam facility can deliver it all!
 substantial opportunity for a step-change in understanding!
Time
domain
Space
domain
Energy
Ion
species
In combination and with chemo/immuno Therapies

## Slide 15: Laser-hybrid Accelerator for Radiobiological Applications
LhARA; a novel, hybrid, approach:
High-flux, laser-driven proton/ion source:
  Overcome instantaneous dose-rate limitation
  Delivers protons or ions in very short pulses:
    Pulse length 10 – 40 ns
  Can provide arbitrary pulse structure
Novel plasma-lens capture & focusing
Fast, flexible, fixed-field post acceleration
  Protons up to 127 MeV p;
  Ions up to ~35 MeV/u
Staged implementation:
  Stage 1: In vitro studies with protons at energies up to 15 MeV
  Stage 2: In vivo & in vitro studies with protons up to 127 MeV and ions up to 33 MeV/u
→ compact, uniquely flexible facility
LhARA consortium
arXiv:2006.00493

## Slide 16: LhARA consortium’s ambition
LhARA will be a uniquely-flexible, novel system that will:
Deliver a systematic and definitive radiobiology programme
Prove the feasibility of the laser-driven hybrid-accelerator approach
Thereby lay the technological foundations for transformation of PBT
  automated, patient-specific: implies online imaging & fast feedback and control

## Slide 17: LhARA
The Laser-hybrid Accelerator for Radiobiological Applications (LhARA)
arXiv:2006.00493

## Slide 18
LhARA
arXiv:2006.00493

## Slide 19: Sheath acceleration
Laser incident on foil target:
  Drives electrons from material
  Creates enormous electric field
Field accelerates protons/ions
  Dependent on nature of target
First observation ~2000
Active development:
  Laser: power and rep. rate
  Target material, transport
Schwoerer, H. et al., 2006; Nature, 439(7075).

## Slide 20: Laser-driven proton/ion source
Advantage:
  Enormous proton/ion flux at 10—15MeV in tiny (25 fs) pulse at up to 10 Hz
Issue to be solved:
  Efficient capture, focusing, selectin and manipulation of divergent ion beam
Ti:Sapphire commercial system >15TW
Pulse ~35fs at rep-rate of at least 10Hz
At least 500mJ laser energy - IL ~ 1020 Wcm-2

## Slide 21: Beam capture/production principle
Plasma (Gabor) lens:
  Strong focusing exploiting electron plasma in solenoid
Posocco, Pozimski
Gabor
1957

## Slide 22: LhARA: ion-source development
Capture
Electron plasma:
  Strong focusing of +ve ions
1st prototype:
  1 MeV protons Surrey Ion Beam Centre
  Aberrations observed
Upgraded prototype:
  Under development Imperial
Laser source/capture test
Integration test:
  Integration test on Imperial Cerberus Laser
Plan:
  “Now”: prepare to validate lens with a
  Next: test using laser-driven source

## Slide 23: LhARA; stage 1
Pasternak
arXiv:2006.00493
arXiv:2006.00493

## Slide 24: LhARA – Stage 2
In-vitro radiobiology using animal models:
  Post-acceleration required
Baseline: fixed field accelerator:
  x3 increase in momentum
    15 MeV protons accelerated to 127 MeV
    3.8 MeV/u carbon 6+ ions accelerated to 33 MeV/u
arXiv:2006.00493

## Slide 25: Fixed Field Accelerator
Advantages over conventional medical cyclotron
  Variable energy operation without energy degraders
  Operation with different ions
  Multiple extraction ports possible
Bending magnetic fields do not vary in time.
  Rapid acceleration.
Alternating gradient gives strong focussing.
Very large acceptance.
  Useful, e.g. to accelerate muon beams.

## Slide 26: FFA potted history
Early 1950s, FFAG developed independently:
  Japan by Tihiro Ohkawa
  US by Keith Symon
  Russia by Andrei Kolomensky.
The first prototype was operated in 1956
  Jones, Terwilliger, Technical Report MURA-LWJ/KMT-5 (MURA-104), April 3, 1956.
Not much activity until first proton accelerator in 2000
PRISM muon beam phase rotation demonstration ring at Osaka.
The Michigan Mark I FFA 400KeV electron accelerator was the first operational FFA.
EMMA at Daresbury
500 keV Proton proof-of-principle FFA at KEK.
Kyoto University FFA for ADSR

## Slide 27: LhARA FFA
arXiv:2006.00493

## Slide 28: Next steps; 5-year R&D plan
5-year plan presented in pre-CDR designed to:
  Address technical risks presented in pre-CDR
    Especially source and plasma-lens capture
    Instrumentation and diagnostics
  Deliver technical designs for the LhARA facility
  End stations.
    Automation, sample handling, imaging
    Simulation, including impact on tissue/tissue response
→ Capability to start Stage 1 in-vitro programme
arXiv:2006.00493

## Slide 29: Conclusions
The Laser-hybrid Accelerator for Radiobiological Applications (LhARA)

## Slide 30: Conclusions
Laser-hybrid approach has potential to:
  Overcome dose-rate limitations of present PBT sources;
  Deliver uniquely flexible facility:
    Range of ion species, energy, dose, dose-rate
  Disruptive/transformative approach to PBT ‘for 2050’ …
Opportunity:
  Develop and prove novel systems in operation;
  Deliver research facility dedicated to radiobiology;
  Contribute to study of biophysics of charged-particle beams
First and next steps:
  Initial concept developed and prototype evaluation underway
  Seeking resources to execute R&D programme laid out in ‘pre-CDR’
  Wonderful opportunity to build novel techniques to ‘spin back in’!