## Slide 1: Accelerator applications for medicine
M.Dosanjh1, I.Konoplev2, K.Long3, S.Sheehy4
1. CERN
2. JAI, Oxford
3. Imperial
4. JAI, Oxford
1. CERN, recently appointed Visiting Professor in Oxford
2. JAI, Oxford
3. Imperial
4. JAI, Oxford

## Slide 2: Medical accelerators; the challenge
Cancer:
  2nd most common cause of death globally
  Radiotherapy is indicated in half of all cancer patients
Anticipated growth in demand:
  14.1 x 106 new cases in 2012 ⇢ 24.6 x 106 by 2030
  8.2 x 106 cancer deaths in 2012 ⇢ 13.0 x 106 by 2030
Demographic:
  Projections above based on reported cases (i.e. HIC)
  Opportunity to save 26.9 x 106 lives in LMIC by 2035
Scale-up in provision:
  Requires development of new and novel techniques
Atun, Lancet Oncol. 2015 Sep;16(10):1153-86

## Slide 3: Medical accelerators; the opportunity
Scale-up in provision:
  Requires development of new and novel techniques
    Investment required will generate substantial economic gains
R&D programme:
  Incremental development of current practice:
    Instrumentation, imaging/image-processing, f/b and control
  System approach to robust, flexible next-generation facilities:
    Multi-species, combined therapies, integrated imaging
    Resilient to e.g. environment, component failure, …
  Collaborative R&D to harness novel techniques:
    Multi-species, combined therapies, UHDR/FLASH, integrated imaging
    Laser-driven, hybrid, novel (e.g. FFA) approaches
Opportunity to contribute to underpinning science and R&D:
  Radiobiology: especially charged particle (p, ion)
  In-situ dose-deposition imaging: especially p, ion
  Integration of planning, on-treatment, imaging, simulation, feedback and control
Atun, Lancet Oncol. 2015 Sep;16(10):1153-86

## Slide 4: Electron linacs for X-ray/e therapy
Accelerator applications for medicine

## Slide 5: Medical linac
Electrons accelerated to 5—10 MeV:
  3 GHz cavity
Delivers e and X-rays:
  X-rays created on internal target
  Intensity-modulated therapy delivered using sophisticated collimation & gantry systems
Substantial initiative:
  “Medical linacs for challenging environments”
    CERN, ICEC, JAI, STFC, …
  Target proposal to GCRF
Investigation of UHDR (FLASH) RT:
  Feasibility of use/modification of linac at CXH for research
    CXH, ICL, ICR, RMH

## Slide 6
M. Dosanhj

## Slide 7: Towards an understanding of the issues
Abuja, Nigeria
S. Sheehy
In preparation

## Slide 8: Medical LINAC: accelerating structure
Objectives:
  Design and build TW 12GHz accelerating structure that is:
    Vacuum sealed, has cathode included
    From 50keV to 8MeV (x-ray bulb)
  Minimise the construction and running cost
  Compatible with permanent magnets
Requirements:
  Stability (no need to retune or service – “light bulb” approach)
  Compactness
  Modularity (same composition as for vacuum tubes used in aviation and industrial applications)
Technical drawing of the prototype
Prototype of the TW accelerating structure
I. Konoplev
Preliminary numerical studies have been carried out.

## Slide 9
Imperial seeks to contribute too!
System/engineering aspects:
  Dyson School of Engineering Design
  Physics
Exploring:
  Contributions to system-engineering; &
  Integration (incl. imaging ‘n’ control)
Not funded.
Regroup in Botswana
S. Sheehy

## Slide 10: Hadron-beam therapy
Accelerator applications for medicine

## Slide 11: The benefit of hadron beams
Relative Biological Effectiveness (RBE):
  Dose required to generate particular biological effect relative to reference radiation

## Slide 12: Medical Beam Line Simulations with BDSIM
Tracking & Optics:
  Particle tracking though Geant4 models of beam lines
    Excellent agreement with accelerator tracking codes
    Beam line optics calculations with full statistical uncertainties
Dosimetry:
  Record particle-matter interactions and energy deposition:
    Energy deposition in beam line, shielding, isocentre target…
    Full tracking of secondary particles
Flexibility:
  User customization
    External geometry and field maps
    Separate tool for user-defined analyses.
Impact:
  Ongoing simulation studies:
    CCAP – LhARA
    CCAP – MedAustron
    IBA
    In-house model (based on PSI Gantry 2)
Degrader for energy selection
Concrete shielding and magnet support block geometry.
Isocentre target volume (water phantom)
Optics
Energy Deposition
Analysis
W. Shields, L. Nevay,
S. Boogert, et al. (RHUL)
Contact: william.shields@rhul.ac.uk
Accelerator Beam Line

## Slide 13: Particle beam therapy
Proton:
  Mostly cyclotron-based
    Issues:
      Energy modulation;
      Shielding
Proton & ion (carbon):
  Synchrotron based:
    Issues:
      Energy modulation
      Source:
        Injector per ion species
        Limit to dose rate
Many initiatives!
  PIMMS2
  LhARA
Christie
MedAustron

## Slide 14: Hadron therapy; the issue of precision
RBE:
  Known to depend on, e.g.:
    Tissue type, energy, dose, dose-rate, ion species …
  Yet:
    For p, RBE=1.1 is used
    For C, less information available
Target (i.e. tissue) fragmentation:
  Protons:
    Delivers radiation distant from beam
  Carbon:
    Substantial & distant contributions and strong tail beyond Bragg Peak
Opportunity!
  Prove new techniques while contributing to basic radibiology
Proton
Carbon

## Slide 15: Laser-hybrid Accelerator for Radiobiological Applications
LhARA; a novel, hybrid, approach:
  High-flux, laser-driven proton/ion source;
  Novel plasma (Gabor) lens capture & focusing
  Post-acceleration with large-dynamic aperture FFA
Unique features:
  Very large flux of p or ions in very short pulses:
    Enormous instantaneous dose
  Inject at ~15 MeV into first accelerating structure
    Overcomes space-charge limit of today’s ion sources
  Staged implementation:
    In-vitro studies permitted at 15 MeV:
      Source, capture, transport
    In-vivo studies using post-accelerator (75 MeV p; ~20 MeV/u)
Uniquely flexible radiobiology facility:
  Many ions, proton to carbon, in single facility
  Wide range of energy and dose rate, allows UHDR/FLASH radiotherapy
Technologies can be developed to create uniquely flexible therapy facility
Original concept: Pozimski

## Slide 16: LhARA; stage 1
Initial layout for first end-to-end simultion.
Now superceded.
Pasternak
Capture @ 10—15 MeV

## Slide 17: LhARA work in progress
Capture
Electron plasma:
  Strong focusing of +ve ions
1st prototype:
  1 MeV protons Surrey Ion Beam Centre
  Aberrations observed
Upgraded prototype:
  Under test in 022
Towards compact design
Capture and transport using Gabor lenses:
  Normal conducting solenoids alternative/risk mitigation
Energy selection based on collimation
Momentum selection in the arc
Switching magnet:
  Select in-vitro or to send beam to post-accelerator

## Slide 18: LhARA SoI to ASB
Modest request; goal:
  CDR in two years
Build case and ‘coalition’:
  Already broad national and international participation

## Slide 19: Conclusions
Accelerator applications for medicine

## Slide 20: Conclusions
JAI has exciting programme in medical accelerators:
  Electron linacs for X-ray/e therapy:
    Medical Linac for Challenging Environments;
    Modification of ‘production’ machine for UHDR/FLASH studies
  Hadron-beam therapy:
    Engagement with PIMMS2 in collaboration with CERN
    Development of unique facility, LhARA
Emerging collaborations JAI ⇠⇢ CCAP/Imperial:
  A growing strength!

## Slide 22: Proton and Ion Medical Machine Study 2
PIMMS2 study start 2019
  Open collaboration with: CERN and SEEIIST
  Resources through EU accession / structural funds
Opportunities:
  Ion source / LEBT;
  Linac/ring
  Gantry, imaging/feedback/control
M. Vretenar (CERN)
M. Vretenar (CERN)