## Slide 1: end-station; Initial specification
K. Long
Imperial College London/STFC
2 October, 2018

## Slide 2: Intro
Starting point for discussion, objective:
  Allow simulation to define minimum beam energy for p, He, Li, C
  Initiate investigation/simulation of sample holders, beam windows and instrumentation to:
    Refine (change!) specification;
    Allow discussion of beam and sample movement schemes
    Begin consideration of sample management and environment control
    Feedback on minimum energy
Exploit work of Laura Murgatroid

## Slide 3: Sample holder
Tray:
  Bespoke, existing, modification of existing?
Concept:
  Multi-well
  Base of well thinned to 100—150 micron
To investigate:
  Material:
    Needs to support cell/culture medium
    Be capable of sterilisation
    Support cell growth
  Handling:
    Stackable
    Appropriate for remote handling

## Slide 4: End-station configuration
Beam/beam window:
  Scanning spot size?
    0.3x0.3 cm2 spot (as at MedAustron) sufficient?
  Minimise thickness (and X0):
    Material; mylar. Can we ‘get away with’ 25—50 microns?
    Sag, bust rate, …
Instrumentation, dose shot-by-shot:
  Only need to instrument window area
  SciFi? 150—250 micron; enough light?
Remote handling:
  x, y, f stages (‘easy’)
  Remote exchange of trays (possible)
  Monitoring, instrumentation of end-station, climate control

## Slide 5: Summary
In path of beam:
  Mylar window: 25—50 micron?
  SciFi: 150—250 micron polystyrene?
  Air: 5mm air gap, plus air between window and SciFi and meniscus to top of flange
  Bottom of sample tray: 100—150 micron?
Sample movement sufficient?
  Beam scanning and sample movement combined?
No limit on depth of culture medium
Discuss!