## Slide 1
Dose Measurement for Beam Tests
John Matheson
Rutherford Appleton laboratory
The Goal: verify simulations with experimental data
Design of an instrumented water phantom for test beam work
  Based on scintillating fibre
  Calibration against dosimetric standards
  Transducers for proton acoustic measurements (later)
Next steps

## Slide 2
SmartPhantom Layout
Aim is to compare measurements:
proton acoustic
scintillating fibre
dosimetry
Compare measurements & simulations:
protons in water (GEANT4)
protons in detectors (GEANT4)
acoustic signals (k-Wave)
Water-filled phantom useful for protons, few 10s of MeV up
www.ptwdosimetry.com
Beam is measured using scintillating fibre planes
Scintillating fibre -> clear fibre -> detector
Aiming to use the edge of the plane as a connector
Clear fibres bundled and sent to CMOS camera
For faster readout, could use photodiodes
From: Medical Applications for Particle Physics (PhD Thesis), H.T.Lau, Imperial College (2021)

## Slide 3
SmartPhantom Simulations (GEANT4)
H.T.Lau
Solid curves – GEANT4 simulated Bragg Peaks at various energies
Coloured points – energy deposited in the scintillating fibres
Dashed curves – Bortfield model used to reconstruct the B.P. from the fibre data

## Slide 4
SmartPhantom construction trials
Prototype planes, wound with fishing line on the winding jig

## Slide 5
SmartPhantom Scintillating Fibre Tests
Beam intensity increasing with time: 59 MeV beam
Beam intensity increasing with time: 11 MeV beam
H.T.Lau
Preliminary tests of scintillating fibre bundle at Clatterbridge

## Slide 6
PTW Markus chamber www.ptwdosimetry.com
Plane parallel ion chamber
Calibrated against primary standard at NPL
Waterproof - can be used in water phantoms
Available at Birmingham Univ. cyclotron
Use to calibrate a transmission ion chamber
Transmission chamber used in routine monitoring
Can be coupled with RCF or alanine dosimetry (relative measurement of dose distribution)
Calibration of SmartPhantom for dosimetry

## Slide 7
NPL – small portable graphite calorimeter
NPL is developing SPGC
Portable primary standard
Prototype tested at RAL CLF
Can be brought to test beams
francesco.romano@ct.infn.it

## Slide 8
The future – next steps
Finalise assembly methods for fibre planes
Identify suitable beam test facility for the scintillating fibre SmartPhantom
Complete SmartPhantom fibre planes and readout assembly
Beam test SmartPhantom, comparing with dosimetric standards
Comparison of SmartPhantom beam test results with GEANT4 simulations
Simulations will be used to develop analysis scripts:
  Find the position of the Bragg peak from data
  Calculate beam profile, LET and dose delivered in real time
Integrate proton acoustic measurements into SmartPhantom
Next round of beam tests to check GEANT4 and k-Wave simulations against beam test data

## Slide 9
Spare Slides

## Slide 10
SmartPhantom Simulations (GEANT4)
Sample output from GEANT4 Simulations showing the energy deposited in each fibre at each plane
H.T.Lau

## Slide 11: SciWire - Scintillating Fibre Detector
STFC Impact Acceleration Account grant to develop scintillating fibre detector for low-energy ion beams.
  Energy measurement.
  Intensity profile.
Plane made of fibres arranged in two layers perpendicular to each other.
5cm
250m
5cm
Detector consists of multiple planes.
Scintillation light from all planes is read out from one side for each orientation.
Sr90
Step a Sr90 source across face of the detector, positioning the source at the centre of a pair of x and y fibres.
Measure position resolution and cross-talk.
Further tests with the laser driven ion beam.
Possibility of dose profiling.

## Slide 12
Energy loss in the end station using the beam tracked from after the capture section.
10 MeV
12 MeV
15 MeV
0.075 mm vacuum window
0.03 mm cell layer
1.15 mm sample
container base
5mm air gap
0.25 mm scintillating fibre layer
15 mm cell nutrient
solution
Stage 1 end station
beam
10 MeV
15 MeV
12 MeV

## Slide 13
Thin ceramic monitors
AlN or SiN membrane 50-150 micron
Chemically etched and metal electrodes deposited
Beam induces currents on the electrodes
Needs some work to define diameter, thickness, mechanics, electrode geometry, readout
Available from industry (Silson, Ametek/HSFoils)
Thanks to Alex Howard