## Slide 1: Analytical designs for the LhARA solenoids (normal-conducting) LhARA fortnightly meeting
16th August 2022
Titus Dascalu

## Slide 2
LhARA Stage 1
Risk mitigation: alternative capture system based on conventional solenoids

## Slide 3
Solenoid requirements
Equivalent field of a solenoid
1st solenoid most demanding
  Choose nominal design with 1 m long coil (Gabor lens flange-to-flange space is 1.157 m)
Solenoids 2 to 5
  Different design (for lower material cost, power consumption)

## Slide 4
Choice of material
Most frequent choice of coil material
Normal conducting
Superconducting

## Slide 5
Choice of material
Normal conducting
Superconducting
Very high current density compared to conventional conductors
Negligible power consumption
Complicated structure: rigid coil former + insulating cryostat (large space requirement around the coil)
The cryostat/cooling infrastructure needs careful maintenance
Cost of superconducting coils is significantly higher than the cost of conventional conductor
(Hollow copper conductor)
Very common design in many accelerator magnets
Efficient cooling
  water in direct contact with the source of heat
Coils potted in resin are typically very robust
Each cable has to be insulated
  adds complexity and requires more space
Weight of the coils is typically high
Cooling and electric circuits are interwoven, but need separation at the their ends
  pressure drop leads to complex cooling circuits for large coils + increased risk of water leakages
Aim of this design exercise: evaluate the requirements and performance of a normal-conducting solenoid that is suitable for LhARA

## Slide 6
Design procedure
Most frequent choice of coil material
Canonical values
Hydraulics calculations
…
Different layers have different cooling requirements

## Slide 7
Graded coil design
Use more than one transverse size for the copper cable
Increase the diameter of the cooling channel in the layers further away from the bore
  by keeping the conducting area constant
2 layers, cable size C
2 layers, cable size B
2 layers, cable size A
A
B
C

## Slide 8
The solenoid for LhARA

## Slide 9
Scaling studies: magnet size
c
Filling factor (typically

## Slide 10
Scaling studies: iron cover mass + power consumption

## Slide 11
400 A magnet design
26 total layers
Graded coil
  3 types of cable
Each point is a different configuration with
  layers, cable type A
  layers, cable type B
  layers, cable type C

## Slide 12
400 A magnet design–specifications
T
27 cm thick coil
1150 kg
155 kW

## Slide 13
1000 A magnet design
14 total layers
Graded coil
  3 types of cable
Each point is a different configuration with
  layers, cable type A
  layers, cable type B
  layers, cable type C

## Slide 14
1000 A magnet design–specifications
T
19 cm thick coil
925 kg
125 kW

## Slide 15
2000 A magnet design–specifications
T
20 cm thick coil
1173 kg
105 kW

## Slide 16
2D FEMM Models
400 A
1000 A
2000 A
400 A
1000 A
coil
cover
Field on axis

## Slide 17
Possible issues

## Slide 18
Space constraints for the 1st solenoid in the beamline
Solenoid mm
  For magnet entrance to be placed 150 mm from target
Different laser incidence angle envisioned for LhARA
  Design will probably allow for more space downstream of target

## Slide 19
Coolant manifold and electricity separation
CERN-SHiP-NOTE-2019-004

## Slide 20
Backup

## Slide 21
Table legend

## Slide 22
Estimate of the cost scaling
Cost scaling based on a procedure from:
  G. Brianti and M. Gabriel, Basic expressions for evaluating iron core magnets – A possible procedure to minimize their cost, CERN/SI/Int. DL/70-10 (1970).
  a few modifications to account for the increase in the power supply with the current
    Assumption: the cost doubles when going from 250A to 1000A
60,000 hours of running (~ 15 years of 12 hours/day)
Iron return yoke/cover included
One power supply per magnet
Equipment cost includes
  Cost of power supply
  Cost of d.c. power distribution
  Cost of cooling
Absolute cost is not specified (only the approximate relations between various cost components)

## Slide 23
Estimate of the cost scaling (per magnet)

## Slide 24
Alternatives

## Slide 25
Alternative designs
Tape wound aluminium coil (anodised surface acts as a complete electrical insulator between the winding layers)
  “sandwich” structure with water cooling spacers
  Nitrogen cooling (100K)
  Aluminium fully in water
  Heat sink outside of magnet (heat transported in the plane of the strip)

## Slide 26
Alternative designs
Tape wound aluminium coil
Pros
  Save space and complexity
  Heat exchanger/cooling circuit is simpler and independent of the electric conductor
  Coil is about 1/3rd of the weight of copper
  Coils of very large size (4m x 1.5m) have been made, but not necessarily with the external cooling facility
Cons
  Lower electrical conductivity, so larger coil is needed
  Strip structure needs to be rigid in the region of contact with the heat sinks to avoid damage to the interface
  Use of very large Al coils is not as well established as the more conventional copper coils

## Slide 27
Manufacturer