## Slide 1
LhARA endstation requirements for in vitro radiobiology research
Dr Jason Parsons
Cancer Research Centre
Department of Molecular and Clinical Cancer Medicine

## Slide 2
  Particle beam therapy (PBT) radiobiology
Bragg peak
Depth in tissue
Relative dose
Distal fall-off
Tumour
Particle energy
LET
  A constant relative biological effectiveness (RBE) value of 1.1 is used in clinical practice. However, there is a large uncertainty with using this approach as RBE is variable and dependent on many factors, including:-
  Proton energy (therefore linear energy transfer, LET) and dose.
  Radiosensitivity/radiobiology of the tissue.
  Biological end-point examined (e.g. clonogenic survival, tumour growth delay).
  Therefore, further research exploiting the biological impact of particles is vital for investigating RBE, and thus improving clinical use of PBT.
Taken from Paganetti and van Luijk (2013) Sem Rad Oncol
Vitti and Parsons (2019) Cancers

## Slide 3
  60 MeV Proton beam and radiobiology facilities at the Clatterbridge Cancer Centre (CCC)

## Slide 4
  58MeV
  Impact of PBT on cell survival and CDD
Chart: hours post-IR
| Control | 0 | 1 | 2 | 4
Proton-IR (58 MeV) | 5.1589 | 26.1002 | 14.9746 | 6.1455 | 5.4946
Proton-IR (58 MeV; modified) | 6.8571 | 28.7597 | 14.5195 | 7.3029 | 5.0197
Proton-IR (11 MeV) | 5.1082 | 28.938 | 15.5107 | 5.5521 | 4.8061
Proton-IR (11 MeV; modified) | 7.557 | 38.4138 | 22.7667 | 16.0721 | 13.5614
****
*
***
**
  58MeV (mod.)
  11MeV
  11MeV (mod.)
Chart: 11 MeV
USP6
Chart: Dose (Gy)
| 0 | 1 | 2 | 4
58 MeV | 1 | 0.80439 | 0.72289 | 0.345
11 MeV | 1 | 0.56082 | 0.40532 | 0.18899
Chart: Dose (Gy)
| 0 | 1 | 2 | 4
58 MeV | 1 | 0.91372 | 0.67115 | 0.31187
11 MeV | 1 | 0.56297 | 0.38605 | 0.1851
  HeLa
  UMSCC6
  SF2, p<0.02
  SF2, p<0.01
  Low energy (relatively high-LET) protons cause significantly reduced cell survival versus high energy (low-LET) protons.
Chart: Dose (Gy)
| 0 | 2 | 4 | 8
NT siRNA | 1 | 0.51952 | 0.23205 | 0.01555
USP6_13 siRNA | 1 | 0.29115 | 0.059284 | 0.0073502
  Carter et al, (2018) IJROBP; Carter et al, (2019) IJROBP
  CDD
  DUB siRNA screen analysing changes in survival post-irradiation.
  siRNA screen for deubiquitylating enzymes (DUBs) revealed that USP6 is required for survival following low energy protons.
  Low energy protons cause increases in CDD formation that persist for >4 h post-irradiation.
11 MeV
11 MeV
Chart: Dose (Gy)
| 0 | 2 | 4 | 8
NT siRNA | 1 | 0.39694 | 0.16487 | 0.011539
PARP-1 siRNA | 1 | 0.11311 | 0.049453 | 0.003046
PARP/USP6_13 siRNA | 1 | 0.1508 | 0.041627 | 0.003817

## Slide 5
  Model for the recognition and repair of CDD in chromatin
Chromatin remodelling/DNA repair protein recruitment
DNA damage -
Site-specific histone modifications
Ub
RNF20/40
High-LET IR
USP6
MSL2
Restoration of DNA integrity
PARP-1
OGG1
PARG
BRCA2
  Carter et al., (2018) IJROBP; Carter et al., (2019) IJROBP

## Slide 6
Using ultra-high dose rates (>100 Gy/s).
Benefits of FLASH radiotherapy
  The underlying mechanism(s) of the FLASH effect are unclear (oxygen depletion, role of DNA damage and repair?).
  Lack of radiobiology research into FLASH PBT (LET impact?) and facilities to perform this.

## Slide 7
Reliable beam with accurate dosimetry (low and FLASH dose rates).
Automation to allow rapid irradiation of large sample numbers.
Precise irradiation relative to the Bragg peak (with increasing LET).
Irradiation in different oxygen conditions (hypoxia; important for FLASH).
Microscopy, particularly enabling time lapse experiments (e.g. DNA damage markers/foci).
Radiobiology research facilities enabling cellular/molecular biology approaches for processing of samples in real-time (minutes-hours).
In vitro end-station requirements