## Slide 1: Introduction
Pre-publication review of the LhARA pre-CDR

## Slide 2: Background
Centre for the Clinical Application of Particles:
  Imperial centre of excellence; established October 2017
  Mission:
    Develop the technologies, systems, techniques and capabilities necessary to deliver a paradigm shift in the clinical exploitation of particles.
  Key objectives:
    Develop novel, compact, laser-driven accelerator systems for clinical applications;
    Deliver the capability to assess the biological and therapeutic efficacy of different ion species; and
    Develop improved diagnostic, dose-measurement, imaging, treatment-planning, data-processing, andmachine-learning techniques.
LhARA, the Laser-hybrid Accelerator for Radiobiological Applications:
  Central to the CCAP’s research and development programme

## Slide 3: Multidisciplinary collaboration
Further interest from:
Groups in the UK and overseas

## Slide 4: Radiotherapy; the challenge
Cancer: second most common cause of death globally
  Radiotherapy indicated in half of all cancer patients
Significant growth in global demand anticipated
Today, most radiotherapy delivered with X-rays
  But, interest in proton and ion beam therapy is increasing

## Slide 5: Particle-beam therapy
Proton and ion-beam therapy:
  Bulk of dose deposited in Bragg peak
  Significant normal-tissue sparing (entry)
  Almost no dose beyond the Bragg peak

## Slide 6: The radiobiology needs to be understood
Treatment planning:
  Based on ‘Relative Biological Effectiveness (RBE)
    Proton-treatment planning uses RBE = 1.1
    Effective values are used for C6+
Paganetti, van Luijk Sem. Rad. Oncol (2013)
Essential: improved, fundamental, understanding of radiobiology
RBE:
Ratio of dose required to gain same biological response as reference photon beam
RBE known to depend on:
Energy, ion species
Dose & dose rate
Tissue type
Biological endpoint

## Slide 7: Particle beam therapy today
Cyclotron based:
  Limitations:
    Energy modulation
    Instantaneous dose rate
Synchrotron based:
  Limitiations:
    Complexity
    Instantaneous dose rate
Christie Hospital Manchester
MedAustron Austria
 reduce footprint, cost and complexity
‘PBT for the many’
 increase flexibility
optimize treatments

## Slide 8: Laser-hybrid Accelerator for Radiobiological Applications
LhARA; a novel, hybrid, approach:
  High-flux, laser-driven proton/ion source:
    Overcome instantaneous dose-rate limitation
    Delivers protons or ions in very short pulses:
      Pulse length 10 – 40 ns
    Can provide arbitrary pulse structure
  Novel plasma-lens capture & focusing
  Fast, fixed-field post acceleration
 compact, uniquely flexible facility
LhARA consortium

## Slide 9: Radiobiology in new regimens
Ambition: LhARA the ideally flexible beam facility that can deliver it all!
 substantial opportunity for a step-change in understanding!
Time
domain
Space
domain
Energy
Ion
species
In combination and with chemo/immuno Therapies

## Slide 10: Our vision and our ambition
Vision:
LhARA will be a uniquely-flexible, novel system that will:
Deliver a systematic and definitive radiobiology programme
Prove the feasibility of the laser-driven hybrid-accelerator approach
Lay the technological foundations for the transformation of PBT
  automated, patient-specific: implies online imaging & fast feedback and control
Ambition:
  Develop:
    necessary techniques, technologies, and systems
  Exploit:
    system approach to bring novel techniques into clinical practice as they mature
  Integrate:
    production prototypes in a production system for radiobiological research
  Engage:
    industry and clinical PBT centres
    during development of techniques, technologies, and systems

## Slide 11: Pre-publication review

## Slide 12: In conclusion
Many thanks for taking part in the review
Many thanks too for your patience and flexibility in the light of the pressures imposed by the Covid-19 pandemic
Agenda for 25Mar20 session of the review: