## Slide 1
Overview of the LhARA Facility
Review of the LhARA pre-CDR
Ajit Kurup
25th March 2020

## Slide 2: Introduction
Overview of the design of the facility.
  Design parameters.
  Accelerator
  End stations
  Diagnostics
Staging.
R&D plan and project schedule.

## Slide 3: Design parameters

## Slide 4: Design parameters

## Slide 5: Accelerator
Capture
Matching and energy selection
BEAM
DUMP
BEAM
DUMP
Beam to the low energy in vitro end station
Beam to the high energy in vitro end station
Beam to the in vivo end station
Beam from the laser target
Fixed field accelerator ring
Injection line
Extraction line
Extraction line matching
In vivo beam line matching
RF cavities for longitudinal phase space manipulation

## Slide 6: Staging
Construction will be done in two stages.
The goal is maximise scientific output.
  Generate scientific output during construction of Stage 1.
  Radiobiology programme using Stage 1 whilst constructing Stage 2.
Beam from laser source
Stage 1
Stage 2

## Slide 7: Laser source
Produces intense beams and multiple species, e.g. proton and carbon ions.
  Overcome space charge limit of conventional sources since beams are produced with energies O(10) MeV.
Issues to consider
  Large energy spread.
  Large divergence.
  Beam stability, especially if laser operated near the limits of its specifications.
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
LASER
Positive ions from hydrocarbon contamination on the target surface
Electron sheath generated by the laser accelerates positive ions from the target
Ion beam
Principle of target normal sheath acceleration (TNSA).
45
Laser driven ion beam simulation using EPOCH.
Energy vs angle with respect to laser beam direction
Notes: At the start we have a laser which is fired at a thin metal target at an angle of 45 deg. This then generates an ion beam from the surface of the target.
Using this method we can produce very intense beams but with a very large angular spread.
Simulations used a beam generated from the same parameters used in the optics design. Beta means small spot size and with this emittance that means you have a beam with a very large divergence.
Need a strong focusing element to prevent the beam being lost.

## Slide 8: Capture
The Gabor lens uses a plasma to generate a strong electro-static focusing field.
Focal point is energy dependent.
Prototype development to study plasma stability, electron density and verify operation in relatively high vacuum.
       
       
       
       
cylindrical
anode
Grounded
end plate
Electron cloud
Grounded
end plate
Solenoid coils
Ion beam
Original Gabor lens prototype was to be tested with the Cerberus laser at Imperial.
Space to insert diagnostics
Notes: What we plan to use to capture these particles is a a Gabor lens. This can provide a very strong focusing field in a short space by utilizing a confined electron plasma.
Schematic of the principle and a prototype at Imperial that we plan to test with a laser-ion beam.
To model in BDSIM
Lines from Jaroslaw’s beam optics code shows Beta_x and Beta_y (a measure of the beam envelope) are on top of each other. The points from BDSIM show the particle tracking simulations are well matched to the optics design.

## Slide 9: Beam transport – Stage 1
Optics design: BeamOptics and MADX.
Particle tracking simulations: BDSIM and GPT.
Energy deposition in the end station: BDSIM.
Alternative design

## Slide 10: Beam transport – Stage 2
Post acceleration done using an Fixed field accelerator (FFA).
  Spiral FFA.
Injection and extraction lines for the FFA.
High energy arc for in vitro
end station.
In vivo beam line.

## Slide 11: Schedule

## Slide 12: Five year R&D plan