## Slide 1: Development of a laser-hybrid approach to the delivery of ion beams for biomedical application
Laser-hybrid Accelerator for Radiobiological Applications to serve the Ion Therapy Research Facility
ITRF
/

## Slide 2: Radiotherapy; the challenge
Cancer: second most common cause of death globally
  Radiotherapy indicated in half of all cancer patients
Significant growth in global demand anticipated:
  14.1 million new cases in 2012 ⇢ 24.6 million by 2030
  8.2 million cancer deaths in 2012 ⇢ 13.0 million by 2030
Scale-up in provision essential:
  Projections above based on reported cases (i.e. high-income countries)
  Opportunity: save 26.9 million lives in low/middle income countries by 2035
Provision on this scale requires:
  Development of new and novel techniques … integrated in a
  Cost-effective system to allow a distributed network of RT facilities
Atun, Lancet Oncol. 2015 Sep;16(10):1153-86

## Slide 3
Our ambition is to:
Deliver a systematic and definitive radiation biology programme
Prove the feasibility of laser-driven hybrid acceleration
Lay the technological foundations for the transformation of PBT
  automated, patient-specific proton and ion beam therapy

## Slide 4: The case for fundamental radiobiology
Relative biological effectiveness:
  Defined relative to reference X-ray beam
  Known to depend on:
    Energy, ion species
    Dose & dose rate
    Tissue type
    Biological endpoint
Yet:
  p-treatment planning uses 1.1
  Effective values are used for C6+
Maximise the efficacy of PBT now & in the future:
  Develop systematic programme of radiobiological measurements
Paganetti, van Luijk (2013)
SemRadOncol

## Slide 5: What is LhARA?
A novel, hybrid, approach:
Laser-driven, high-flux proton/ion source
  Overcome instantaneous dose-rate limitation
    Capture at >10 MeV
  Delivers protons or ions in very short pulses
    Bunches as short as 10—40 ns
  Triggerable; arbitrary pulse structure
Novel “electron-plasma-lens” capture & focusing
  Strong focusing (short focal length) without the use of high-field solenoid
Fast, flexible, fixed-field post acceleration
  Variable energy
    Protons: 15—127 MeV
    Ions: 5—34 MeV/u
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 6
C. Hill et al; ASTeC/TD DL

## Slide 7: Source: simulation
R&D objectives:
“Full-scale” tests in conditions approaching LhARA specification
LhARA-focused diagnostic and targetry development
High-repetition rate, automation and longevity studies
Accurate numerical modelling 3D simulation codes
PhysRevLett.90.185002
Realistic, 2-stage simulation on ARCHER2 using accurate “pre-plasma” profile
Study proton production as a function of angle of incidence, spot size, proton-layer thickness
Seek to benchmark against data
Dascalu, Dover, Gray

## Slide 8: Source: experiment
R. Gray
Laser energy

## Slide 9: Source: diagnostics & high rep-rate
Diagnostics
High-rep rate / longevity …
Scintillators: key for high rep rate operation
Dedicated calibration effort led by N. Dover (ICL):
  Birmingham MC40 cyclotron

## Slide 10: Capture
“Electron-plasma” (Gabor) lens:
  Strong focusing exploiting electron gas in “Penning/Malmberg” trap
Gabor
1957
Ruksasakchai, Isaac, Eriksson, Bertsche

## Slide 11: Capture
Key issues:
  Electron density, plasma stability
Measurements on Penning-Malmberg trap at Swansea University
  “Rotating wall” to “spin-up” plasma to gain stability
Ongoing campaign:
  Improved diagnostics
  Numerical analysis to interpret and optimise experiments
Ruksasakchai, Isaac,
Eriksson, Bertsche

## Slide 12: Real-time dose measurment
Maxouti, Bamber, Cox, Hobson

## Slide 13: Real-time dose measurement
Maxouti, Bamber, Cox, Hobson

## Slide 14: Stage 2: FFA & FFA magnet
FFA magnet
Emerging collaboration with ISIS u/g team
T.J. Kuo
Pasternak, Shields, Kuo, Kurup, Hill

## Slide 15: Conclusions
Significant progress in ITRF/LhARA:
  Beamline design and optimisation
  Engineering, initial studies of FFA magnet
  Initial characterisation of laser-driven source
  Progress on understanding and stablisation of plasma for Gabor lens
  Design of ion-acoustic proof-of-principle experiment
  Peer-group consultation leading to specification of end-station
Looking forward:
  Recognition of importance of development of biological programme:
    First steps in design and specification of proof-of-principle experiment as part of broader radiation-biology programme
  Project programme for next two years defined
Exciting programme, but, clear need to make the case!

## Slide 17: Backup

## Slide 18: Learning from history
@BioTech:
  Develop the system!
@ energy frontier:
  Innovate through applications:
    Can take greater technical risk
    Reduced timescales, more & more novel machines
    Recruitment & retention, education, and training
Radiology 47:487–91 (1946)
Wilson, then at Harvard designing 150 MeV cyclotron:
Identified benefits and properties of proton beams for RT
Pointed out potential of ions (carbon) and electrons