## Slide 1
a transformational approach to precision, personalised particle-beam therapy

## Slide 2: Hadron beams for radiation therapy
Wilson, then at Harvard designing 150 MeV cyclotron:
  Identified benefits and properties of proton beams for RT
  Pointed out potential of ions (carbon) and electrons
Robert R. Wilson
Radiology 47:487–91 (1946)

## Slide 3: Evolving state of the art
Cyclotron
Laurence; 1932
Synchrotron
Goward, Barnes; 1946
Biological studies; 1948
Clinical studies (pituitary gland);
1954
Cancer therapy
(Mass Gen Hosp)
1974

## Slide 4: Particle beam therapy today
Cyclotron based
Synchrotron based
Christie Hospital Manchester
MedAustron Austria

## Slide 5: Potential benefit of new regimens
FLASH
Conventional regime : ~2 Gy/min
FLASH regime (p) : >40 Gy/s
Evidence of normal-tissue sparing while tumour-kill probability is maintained:
i.e. enhanced therapeutic window
Time line:
Reports: 2014 (e.g. Flauvadon et al, STM Jul 2014)
Confirmation in mini-pig & cat: 2018 (Clin. Cancer Research 2018)
First treatment 2019 (Bourhis et al, Rad.Onc. Oct 2019)

## Slide 6: Potential benefit of new regimens
Worked example: micro beams
Conventional regime : > 1 cm diameter; homogeous
Microbeam regime : < 1 mm diameter; no dose between ‘doselets’
Remarkable increase of normal rat brain resistance.
[Dilmanian et al. 2006, Prezado et al., Rad. Research 2015]
Dose escalation in the tumour possible – larger tumor control probability

## Slide 7: Radiotherapy; the challenge
Cancer: second most common cause of death globally
  Radiotherapy indicated in half of all cancer patients
Significant growth in global demand anticipated:
  14.1 million new cases in 2012 ⇢ 24.6 million by 2030
  8.2 million cancer deaths in 2012 ⇢ 13.0 million by 2030
Scale-up in provision essential:
  Projections above based on reported cases (i.e. high-income countries)
  Opportunity: save 26.9 million lives in low/middle income countries by 2035
Provision on this scale requires:
  Development of new and novel techniques … integrated in a
  Cost-effective system to allow a distributed network of RT facilities
Atun, Lancet Oncol. 2015 Sep;16(10):1153-86

## Slide 8: The case for fundamental radiobiology
Relative biological effectiveness:
  Defined relative to reference X-ray beam
  Known to depend on:
    Energy, ion species
    Dose & dose rate
    Tissue type
    Biological endpoint
Yet:
  p-treatment planning uses 1.1
  Effective values are used for C6+
Maximise the efficacy of PBT now & in the future:
  Require systematic programme to develop full understanding of radiobiology
Paganetti, van Luijk (2013)
SemRadOncol

## Slide 9: Radiobiology in new regimens
The ideally flexible beam facility can deliver it all!
 substantial opportunity for a step-change in understanding!
Time
domain
Space
domain
Energy
Ion
species
In combination and with chemo/immuno Therapies
Multidisciplinary approach essential

## Slide 11: Laser-hybrid Accelerator for Radiobiological Applications
A novel, hybrid, approach:
Laser-driven, high-flux proton/ion source
  Overcome instantaneous dose-rate limitation
    Capture at >10 MeV
  Delivers protons or ions in very short pulses
    Bunches as short as 10—40 ns
  Triggerable; arbitrary pulse structure
Novel “electron-plasma-lens” capture & focusing
  Strong focusing (short focal length) without the use of high-field solenoid
Fast, flexible, fixed-field post acceleration
  Variable energy
    Protons: 15—127 MeV
    Ions: 5—34 MeV/u
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 12
 compact, uniquely flexible facility
N. Bliss (DL)
Draft
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 13: Sheath acceleration
Laser incident on foil target:
  Drives electrons from material
  Creates enormous electric field
Field accelerates protons/ions
  Dependent on nature of target
Active development:
  Laser: power and rep. rate
  Target material, transport
Schwoerer, H. et al., 2006; Nature, 439(7075).

## Slide 14: Many initiatives in Americas, Europe, Asia
Applications in biological research, ambition to push toward clinical application …
  Phys Lett A. (2002) 299:240–7. doi: 10.1016/S0375-9601(02)00521-2
  Med Phys. (2003) 30:1660–70. doi: 10.1118/1.1586268
  Med Phys. (2004) 31:1587–92. doi: 10.1118/1.1747751
  Science. (2003) 300:1107–111
  New J Phys. (2010) 12:85003. doi: 10.1088/1367-2630/12/8/085003
  Phys Med Biol. (2011) 56:6969–82. doi: 10.1088/0031-9155/56/21/013
  Appl Phys Lett. (2011) 98:053701. doi: 10.1063/1.3551623
  Appl Phys Lett. (2012) 101:243701. doi: 10.1063/1.4769372
  AIP Adv. (2012) 2:011209. doi: 10.1063/1.3699063
  Appl Phys B. (2013) 110:437–44. doi: 10.1007/s00340-012-5275-3
  Appl Phys B. (2014) 117:41–52. doi: 10.1007/s00340-014-5796-z
  Radiat Res. (2014) 181:177–83. doi: 10.1667/RR13464.1
  Phys Rev Acceler Beams. (2017) 20:1–10. doi: 10.1103/PhysRevAccelBeams.20.032801
  J Instrum. (2017) 12:C03084. doi: 10.1088/1748-0221/12/03/C03084
  A-SAIL Project. (2020). Available online at: https://www.qub.ac.uk/research-centres/A-SAILProject/
  Vol. 8779. Prague: International Society for Optics and Photonics. SPIE (2013). p. 216–25.
  Vol. 11036. International Society for Optics and Photonics. SPIE (2019). p. 93–103.
  Nuovo Cim C. (2020) 43:15. doi: 10.1393/ncc/i2020-20015-6
  10th International Particle Accelerator Conference. Melbourne, VIC (2019). p. TUPTS005
  …
I will not attempt a review, choosing instead to focus on opportunity
A selection …

## Slide 15: Laser-driven beams for rbio: example 1
DOI: 10.1038/s41598-020-65775-7
Draco:
  Petawatt laser
    E = 13 J, τ = 30 fs, 3 μm FWHM
Beam line:
  Target Normal Sheath Acceleration (TNSA)
  Pulsed solenoid focusing
    19.5T, 2 or 3 pulses/min.
    S1, S2: 40 mm bore
    Half angle acceptance 14o
  Measured transmission (18.6 MeV p)
    50.6% (dual solenoid)
    28.6% (single solenoid)
On Draco @ HZDR

## Slide 16: Laser-driven proton/ion source
Commercial laser:
  Motivation: risk management
Ti:Sapphire commercial system >150TW
Pulse ~35 fs at rep-rate of at least 10Hz
At least 500mJ laser energy - IL ~ 1020 Wcm-2
HT Lau
Thesis, 2022
H.T. Lau

## Slide 17: LhARA Capture
“Electron-plasma” (Gabor) lens:
  Strong focusing exploiting electron gas in “Penning/Malmberg” trap
Posocco, Pozimski
Gabor
1957
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 18
VSIM/BDSIM:
evaluation of m = 1
diocotron mode
Dascalu

## Slide 19: Beam envelopes Stage 1
Propagation of “semi-realistic” source distribution:
  Generated using SMILEI
  Optimisation studies on going
HT Lau, IPAC 2021, WEPAB139

## Slide 20: Rapid, flexible acceleration for stage 2
Fixed-field alternating-gradient accelerator (FFA):
  Invented in 1950s
    Kolomensky, Okhawa, Symon
  Compact, flexible solution:
    Multiple ion species
    Variable energy extraction
    High repetition rate (rapid acceleration)
    Large acceptance
  Successfully demonstrated:
    Proof of principle at KEK
    Machines at KURNS
    Non-scaling PofP EMMA (DL)
LhARA FFA
10 cells
2 MA loaded RF cavities
Dimensions in m
Evolution of RACCAM design; prototype magnet demonstrated
bh
bv
h
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 21: LhARA @ the Ion Therapy Research Facility
Submitted to UKRI Infrastructure Advisory Committee
14 June 2021
N. Bliss (DL)
N. Bliss (DL)
N. Bliss (DL)
Draft
Draft
Draft

## Slide 22: Proposal for LhARA contributions to Preliminary Activity and ITRF Preconstruction Phase
To serve ITRF: 2 + 3-year project in 6 work packages:
  Project Management
  Laser-driven proton and ion source
  Proton and ion capture
  Real-time dose-deposition profiling
  Novel, automated, end-station development
  Facility design and integration
Finalised 01Jun22: CCAP-TN-10
Requested resources for 2-year preliminary phase;
Identified need for further 3-year preconstruction phase

## Slide 23: Preliminary & Preconstruction Phase proposal summary
Preliminary Phase
will start October 2022

## Slide 24: Conclusions
LhARA; the Laser-hybrid Accelerator for Radiobiological Applications

## Slide 25
2040
2050
1970
1980
1990
2000
2010
2020
2030
Novel accelerator techniques
System: image processing
fast feedback, control
Fundamental
radiobiology

## Slide 26: Conclusions
Laser-driven sources are disruptive technologies …
  With the potential to drive a step-change in clinical capability
Laser-hybrid approach has potential to:
  Overcome dose-rate limitations of present PBT sources
  Deliver uniquely flexible facility:
    Range of: ion species; energy; dose; dose-rate; time; and spatial distribution
  Be used in automated, triggerable system → reduce requirement for large gantry
    Disruptive/transformative approach to “distributed PBT for 2050”
To serve the ITRF, the LhARA collaboration now seeks to:
  Prove the novel laser-hybrid systems in operation
  Contribute to the study of the biophysics of charged-particle beams
    Enhance treatment planning
  Create novel capabilities to ‘spin back in’ to science and innovation

## Slide 27: Acknowledgements
ITRF team: N. Bliss, J. Clarke, K. Kirkby, M. Noro, H. Owen