## Slide 2: Plan
Challenges and opportunities
Radiobiology
LhARA
Conclusions

## Slide 3: Challenges and opportunities
The Laser-hybrid Accelerator for Radiobiological Applications (LhARA)

## Slide 4: Radiotherapy; the challenge
Cancer: second most common cause of death globally
  Radiotherapy indicated in half of all cancer patients
Significant growth in global demand anticipated:
  14.1 million new cases in 2012 ⇢ 24.6 million by 2030
  8.2 million cancer deaths in 2012 ⇢ 13.0 million by 2030
Scale-up in provision essential:
  Projections above based on reported cases (i.e. high-income countries)
  Opportunity: save 26.9 million lives in low/middle income countries by 2035
Provision on this scale requires:
  Development of new and novel techniques … integrated in a
  Cost-effective system to allow a distributed network of RT facilities
Atun, Lancet Oncol. 2015 Sep;16(10):1153-86

## Slide 5: The benefit of particles
Maximise therapeutic benefit by:
  Maximising damage to tumour
  Minimising damage to healthy tissue
X-ray therapy:
  Modality used in most radiotherapy
  Dose falls exponentially with depth
  Proximity of sensitive organs limits dose to tumour

## Slide 6: Particle-beam therapy
Proton and ion-beam therapy:
  Bulk of dose deposited in Bragg peak
  Significant normal-tissue sparing (entry)
  Almost no dose beyond the Bragg peak

## Slide 7: The need for a step-change in capability
Growing recognition of benefits of PBT worldwide:
  70 PBT centres in operation; 40 under construction
‘Incremental’ development of technique
  Existing suppliers
  New initiatives
Exciting indications of benefits of novel beams …

## Slide 8: Particle beam therapy today
Cyclotron based:
  Limitations:
    Energy modulation
    Instantaneous dose rate
Synchrotron based:
  Limitiations:
    Complexity
    Instantaneous dose rate
Christie Hospital Manchester
MedAustron Austria
 reduce footprint, cost and complexity
‘PBT for the many’!
 increase flexibility
optimize treatments

## Slide 9
Historical interlude

## Slide 10: Hadron beams for radiation therapy
Wilson, then at Harvard designing 150 MeV cyclotron:
  Identified benefits and properties of proton beams for RT
  Pointed out potential of ions (carbon) and electrons
Robert R. Wilson
Radiology 47:487–91 (1946)

## Slide 11: Evolving state of the art
Cyclotron
Laurence; 1932
Synchrotron
Goward, Barnes; 1946
Biological studies; 1948
Clinical studies (pituitary gland);
1954
Cancer therapy
(Mass Gen Hosp)
1974

## Slide 12: Radiobiology
The Laser-hybrid Accelerator for Radiobiological Applications (LhARA)

## Slide 13: The case for fundamental radiobiology
Relative biological effectiveness:
  Defined relative to reference X-ray beam
  Known to depend on:
    Energy, ion species
    Dose & dose rate
    Tissue type
    Biological endpoint
Yet:
  p-treatment planning uses 1.1
  Effective values are used for C6+
Maximise the efficacy of PBT now & in the future:
  Require systematic programme to develop full understanding of radiobiology
Paganetti, van Luijk (2013)
SemRadOncol

## Slide 14: Biological impact from the physics of ionisation
Low-LET radiation:
  Repairable single/double strand breaks
High-LET radiation:
  Complex DNA lesions
    Multiple DNA pathways
    More difficult to repair
    Enhances cell death
Programmatic approach:
  Dynamic studies of impact of radiation
  Interpret with advanced computer models (e.g. G4DNA)

## Slide 15: Radiobiology in new regimens
Worked example: FLASH
Conventional regime : ~2 Gy/min
FLASH regime : >40 Gy/s
Evidence of normal-tissue sparing while tumour-kill probability is maintained:
i.e. enhanced therapeutic window
Time line:
Initial reports: 2014 (e.g. Flauvadon et al, STM Jul 2014)
Confirmation in mini-pig & cat: 2018 (Clin. Cancer Research 2018)
First treatment 2019 (Bourhis et al, Rad.Onc. Oct 2019)

## Slide 16: Radiobiology in new regimens
Prezado; 13Nov19
Worked example: micro beams
Conventional regime : > 1 cm diameter; homogeous
Microbeam regime : < 1 mm diameter; no dose between ‘doselets’
Remarkable increase of normal rat brain resistance.
[Dilmanian et al. 2006, Prezado et al., Rad. Research 2015]
Dose escalation in the tumour possible – larger tumor control prob.

## Slide 17: Radiobiology in new regimens
The ideally flexible beam facility can deliver it all!
 substantial opportunity for a step-change in understanding!
Time
domain
Space
domain
Energy
Ion
species
In combination and with chemo/immuno Therapies
Multidisciplinary approach essential

## Slide 19: Laser-hybrid Accelerator for Radiobiological Applications
A novel, hybrid, approach:
Laser-driven, high-flux proton/ion source
  Overcome instantaneous dose-rate limitation
    Capture at >10 MeV
  Delivers protons or ions in very short pulses
    Bunches as short as 10—40 ns
  Triggerable; arbitrary pulse structure
Novel “electron-plasma-lens” capture & focusing
  Strong focusing (short focal length) without the use of high-field solenoid
Fast, flexible, fixed-field post acceleration
  Variable energy
    Protons: 15—127 MeV
    Ions: 5—34 MeV/u
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 20
 compact, uniquely flexible facility
N. Bliss (DL)
Draft
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738
N. Bliss et al

## Slide 21: Our vision and our ambition
LhARA will be a uniquely-flexible, novel system that will:
Deliver a systematic and definitive radiobiology programme
Prove the feasibility of the laser-driven hybrid-accelerator approach
Lay the technological foundations for the transformation of PBT
  automated, patient-specific: implies online imaging & fast feedback and control

## Slide 22: LhARA
The Laser-hybrid Accelerator for Radiobiological Applications (LhARA)

## Slide 23: Sheath acceleration
Laser incident on foil target:
  Drives electrons from material
  Creates enormous electric field
Field accelerates protons/ions
  Dependent on nature of target
Active development:
  Laser: power and rep. rate
  Target material, transport
Schwoerer, H. et al., 2006; Nature, 439(7075).

## Slide 24: Laser-driven beams for rbio: example 1
DOI: 10.1038/s41598-020-65775-7
Draco:
  Petawatt laser
    E = 13 J, τ = 30 fs, 3 μm FWHM
Beam line:
  Target Normal Sheath Acceleration (TNSA)
  Pulsed solenoid focusing
    19.5T, 2 or 3 pulses/min.
    S1, S2: 40 mm bore
    Half angle acceptance 14o
  Measured transmission (18.6 MeV p)
    50.6% (dual solenoid)
    28.6% (single solenoid)
On Draco @ HZDR

## Slide 25: Laser-driven beams for rbio: example 2
DOI 10.1038/s41598-022-05181-3
Berkeley Lab Laser Accelerator (BELLA):
  Petawatt laser
    E = 35 J, τ = 35 fs, 52 μm FWHM
Beam line:
  Target Normal Sheath Acceleration (TNSA)
  Active plasma lens focusing
    1 mm diameter Ar gas filled capillary
    33 mm length
    13 mm behind the tape drive target
    ~0.2% transport efficiency for protons with E > 1.5 MeV
On BELLA @ Berkeley

## Slide 26: Capture
Variety of initiatives; some key examples
On PHELIX @ GSI
DOI: 10.1063/1.3299391
DOI: 10.1103/PhysRevSTAB.14.121301
DOI: 10.1103/PhysRevSTAB.16.101302
DOI: 10.1103/PhysRevSTAB.17.031302
NIMA 909 (2018) 173–176
LIGHT – Laser Ion Generation, Handling and Transport
PHELIX:
  Petawatt High-Energy Laser for Heavy Ion EXperiments
    E < 25 J, τ = 500 fs, I > 1019 J/cm2
LIGHT:
  Target Normal Sheath Acceleration (TNSA)
  Ion beam is collimated by a pulsed high-field solenoid
  Phase rotation in RF cavity
  Final focus with a second pulsed high-field solenoid
https://www.gsi.de/work/forschung/appamml/plasmaphysikphelix/experimente/light

## Slide 27: Capture
Variety of initiatives; some key examples
DOI: 10.1103/PhysRevAccelBeams.22.061302
DOI: 10.1103/PhysRevAccelBeams.23.121304
Compact Laser Plasma Accelerator (CLAPA):
  Petawatt laser
    E = 1.3 J, τ = 30 fs, 5 μm FWHM
Beam line:
  Target Normal Sheath Acceleration (TNSA)
  Quadrupole triplet focusing
  Measured transmission:
    88% transmission through triplet
    ±50 mrad collection angle @ 5 MeV
On CLAPA @ Peking University

## Slide 28: ELIMAIA-ELIMED
Extreme Light Infrastructure, Prague, Czech Republic:
ELI Multidisciplinary Applications of laser-Ion Acceleration (ELIMAIA)
  ELI MEDical and multidisciplinary applications (ELIMED)
    ELIMAIA section dedicated to ion focusing, selection, characterization, and irradiation
  Proton energies from 5 to 250 MeV transported to in-air section
Quantum Beam Sci. 2018, 2, 8; doi:10.3390/qubs2020008
Frontiers in Phys. Med. Phys. & Imag. – doi: 10.3389/fphy.2020.564907

## Slide 29: Proposal for LhARA contributions to Preliminary Activity and ITRF Preconstruction Phase
To serve ITRF: 2 + 3-year project in 6 work packages:
  Project Management
  Laser-driven proton and ion source
  Proton and ion capture
  Real-time dose-deposition profiling
  Novel, automated, end-station development
  Facility design and integration
Finalised 01Jun22: CCAP-TN-10
Requested resources for 2-year preliminary phase;
Identified need for further 3-year preconstruction phase

## Slide 30: LhARA laser-driven proton/ion source
Commercial laser:
  Motivation: risk management
Ti:Sapphire commercial system >150TW
Pulse ~35 fs at rep-rate of at least 10Hz
At least 500mJ laser energy - IL ~ 1020 Wcm-2
HT Lau
Thesis, 2022
H.T. Lau

## Slide 31
2-year Programme: Characterising Source and Benchmarking Simulations
J.S Green et al., NJP. 12 (2010) 085012
R. Prasad et al., Nucl. Instrum. Methods. 623.2 (2010): 712-715.
Established Diagnostics…
Established Targetry…moving toward Hz-level targetry
Typical 9-target array
Tape targetry system (online in SCAPA 2022)
….to build a systematic parameter space map of the source performance
Energy, Flux, Divergence across multiple ion species
..but also need to consider some other experimental contributions like temporal contrast
E. Boella, N. Dover, R. Gray et al

## Slide 32
Subsequent 3-year Programme: Producing a stable, high-rep source
D. Marsical et al. , Plasma Phys. Control. Fusion 63 (2021) 114003
Courtesy of C. Palmer (QUB)
Novel Liquid Targetry
ML/AI Control & Optimisation
Implementation of advanced (existing) particle diagnostics, taking account of long term operation.
Implementation of full laser diagnostic suite to support automation, stabilisation.
Reduces production of debris
Increases operational time and possible rep rate
Advanced Particle & Laser Diagnostics
Application of ML techniques (e.g Bayesian Optimisation) for parameter space
Application of AI techniques (DNNs, CNNs) for system control and virtual diagnostics
E. Boella, N. Dover, R. Gray et al

## Slide 33: LhARA Capture
“Electron-plasma” (Gabor) lens:
  Strong focusing exploiting electron gas in “Penning/Malmberg” trap
Posocco, Pozimski
Gabor
1957
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 34
VSIM/BDSIM:
evaluation of m = 1
diocotron mode
Dascalu

## Slide 35: Stability Density
Objectives.
Initial experiments – establish stable high ‘fill factor’ plasmas
Phase 2. New apparatus to access higher densities - Tests at SCAPA
2-year Programme: understand stability, increase plasma density
C. Baker, W. Bertsche et al

## Slide 36: Plasma in ALPHA for production
E-field & large radius deleterious
  Low density
  Small radius
Experimental diagnosis
  MCP imaging
  Mode analysis
Modelling
Manipulation techniques
  Cooling (evaporative)
  Rotating wall
  Feedback/damping
doi: 10.1103/PhysRevLett.120.025001 doi: 10.1016/j.nima.2003.09.052
doi: 10.1063/1.4801067 doi: 10.1103/PhysRevLett.106.145001
doi: 10.1103/PhysRevLett.100.203401
C. Baker, W. Bertsche et al
Notes: ALPHA want’s near axis particles/plasma with low fields/energies.
Opposite to Gabor lens but control & understanding is is critical to achieving success
Heavily diagnosed experiment with powerful e.g. MCP imaging & modes analysis of trapped plasma
Experimental diagnosis backed up with theory & computational modelling
These diagnosis have enabled manipulation techniques to be implemented – such as RW (see plasma density increases) & SDREVC (notice reproducibility of plasma)
Significantly improving study of systematics & subsequent improvements

## Slide 37
Rw = 2.86cm
(Rp/Rw < 0.2)
1014 – 1015 m-3
C. Baker, W. Bertsche et al
Notes: Lower densities (10^14 m^-3), and <20% fill factors, but stored for ‘weeks’. Tesla level fields. 5-20cm length.

## Slide 38: Year 5 milestone
Current
Year 2
Year 5
Final
Subsequent 3-year Programme: develop plasma parameters required for LhARA
C. Baker, W. Bertsche et al
Notes: End of 5th year milestone is to have studied plasma that have focal lengths of a few metres, comparable to many of the lens elements.
Know which 1-2 parameters need to be improved by x2 to reach final ~1m focal length lens. This is opposed to the decades improvement of many parameters needed to reach here.

## Slide 39: Beam envelopes Stage 1
Propagation of “semi-realistic” source distribution:
  Generated using SMILEI
  Optimisation studies on going
HT Lau, IPAC 2021, WEPAB139
J. Pasternak, W. Shields et al

## Slide 40: Rapid, flexible acceleration for stage 2
Fixed-field alternating-gradient accelerator (FFA):
  Invented in 1950s
    Kolomensky, Okhawa, Symon
  Compact, flexible solution:
    Multiple ion species
    Variable energy extraction
    High repetition rate (rapid acceleration)
    Large acceptance
  Successfully demonstrated:
    Proof of principle at KEK
    Machines at KURNS
    Non-scaling PofP EMMA (DL)
LhARA FFA
10 cells
2 MA loaded RF cavities
Dimensions in m
Evolution of RACCAM design; prototype magnet demonstrated
bh
bv
h
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738
J. Pasternak, W. Shields et al

## Slide 41: LhARA @ the Ion Therapy Research Facility
Submitted to UKRI Infrastructure Advisory Committee
14 June 2021
N. Bliss (DL)
N. Bliss (DL)
N. Bliss (DL)
Draft
Draft
Draft

## Slide 42: WP4: Ion-acoustic dose mapping
J. Bamber, E. Harris, M. Maxouti, et al

## Slide 43
Ion Acoustic Dose Mapping
Is it possible to get the deposited dose using acoustic measurements ?
Compatibility with medical ultrasound and possibility of use in vivo

## Slide 44
60.34 mm
55.77 mm
1844.7 mm
100 mm
332 T/m
318.5 T/m
10 mm bore diameter
LION beamline - BDSIM
Figure 3: Side-on view of LION beamline in BDSIM
2x quadropole magnets for focusing
M. Maxouti, et al

## Slide 45
Generate angular distribution
source.txt
Source
Figure 4: Energy distribution of protons from source – simulated and analytic closely match
M. Maxouti, et al

## Slide 46
Simulated Bragg peak
Figure 5: Bragg peak in SmartPhantom, as simulated in BDSIM
M. Maxouti, et al
Initial simulation; take 20 MeV protons with 2% energy spread

## Slide 47
SmartPhantom in Geant4
100 mm
160 mm
140 mm
Beam
(test_file.dat)
Water
Aluminium
Kapton entry window
15 mm
Figure 8: Geant4 simulation of the SmartPhantom. Angled view (left), cross-section view (right)
15 mm
Proof of principle experiment:
liquid scintillator
M. Maxouti, et al

## Slide 48
Acoustic detector array
Figure 11: 7mm diameter acoustic sensor with 300 disc elements each with 2mm diameter. Side view (left) and top view (right).
M. Maxouti, B. Cox et al

## Slide 49
Iterative time-reversal
Figure 14: Reconstructed pressure distribution using an iterative time reversal algorithm
M. Maxouti, et al

## Slide 50: WP5 – End station development & Instrumentation

## Slide 51
User engagement – Peer group consultation.
Automated Handling
Controlled atmosphere
Acoustic Imaging
Cellular imaging
In-vivo irradiation
Brm MC40 cyclotron operation for testing and de-risking.
Beamline instrumentation
Gas jet beam profiler.
Dosimetry verification

## Slide 52: Conclusions
The Laser-hybrid Accelerator for Radiobiological Applications (LhARA)

## Slide 53
2040
2050
1970
1980
1990
2000
2010
2020
2030
1946
↓
1960
Novel accelerator techniques
System: image processing
fast feedback, control
Fundamental
radiobiology

## Slide 54
Novel accelerator techniques
System: image processing
fast feedback, control
Fundamental
radiobiology

## Slide 55: Conclusions
Laser-hybrid approach has potential to:
  Overcome dose-rate limitations of present PBT sources;
  Deliver uniquely flexible facility:
    Range of ion species, energy, dose, dose-rate
  Disruptive/transformative approach ‘for 2050’ …
Opportunity:
  Develop and prove novel systems in production system;
  Deliver research facility dedicated to radiobiology;
  Contribute to study of biophysics of charged-particle beams
First and next steps:
  Initial concept developed and prototype evaluation underway
  Working towards ‘CDR’ for LhARA
  Wonderful opportunity to build novel techniques to spin back in!