## Slide 1: Ionacoustics
LhARA & LMU Meeting
23rd February 2023

## Slide 2
Simulation Pipeline

## Slide 3
BDSIM

## Slide 4
LION beamline - BDSIM
Figure 1: Render of LION beamline at Ludwig-Maximillian University Munich in BDSIM
source
(python file)
2x quadropole magnets for focusing
SmartPhantom

## Slide 5
Source – Energy Distribution
Figure 2: Energy distribution of protons from source – simulated and analytic closely match

## Slide 6
Source – Angular Distribution
Figure 3: Angular distribution of protons from source

## Slide 7
LION beamline - BDSIM
Figure 4: Side-on view of LION beamline in BDSIM
10 mm bore diameter
2x quadropole magnets for focusing
318.5 T/m
332 T/m
60.34 mm
55.77 mm
1728.59 mm

## Slide 8
Quadrupole Acceptance
Figure 5: Diagram to show the accepted particles for the BDSIM simulation of the LION beamline
60.34 mm
5 mm
source

## Slide 9
Shielding
Figure 6: Aluminium shielding with elliptical aperture for quadrupole magnet protection
(taken from Thomas Roesch’s thesis)
acceptancex
acceptancey
6 mm
3 mm

## Slide 10
5e5 protons at the source
Exponential energy distribution
Flat angular distribution
49.72 mrad acceptance in the x-direction
24.86 mrad acceptance in the y-direction
Running the Simulation

## Slide 11
∼1/6 particles enter phantom
Particle depth
Figure 7: Particle depletion through simulated beamline
SmartPhantom
shielding
85883
quadropoles

## Slide 12
Energy Distribution – end of beamline
Figure 8: Energy spectrum of the particles that arrive at the end of the LION beamline

## Slide 13
BDSIM Dose Deposition Profile
Figure 9: Dose depositions in SmartPhantom, as simulated in BDSIM

## Slide 14
Output File
Figure 10: Side-on view of LION beamline in BDSIM
test_file.dat
Accept x & y coordinate particles that fall into the entrance window hole (15 mm diameter)

## Slide 15
GEANT4

## Slide 16
SmartPhantom in Geant4
100 mm
160 mm
140 mm
Beam
(test_file.dat)
Water
Aluminium
Kapton entry window
15 mm
Figure 11: Geant4 simulation of the SmartPhantom. Angled view (left), cross-section view (right)
15 mm

## Slide 17
Geant4 Energy Distribution
Figure 12: Binned energy depositions along the three axis (0.1 mm voxels)
FWHM ~ 2.1 mm
FWHM ~ 1.2 mm

## Slide 18
k-Wave

## Slide 19
3D Energy Distribution
Figure 13: Distribution caused by the proton beam energy depositions

## Slide 20
Acoustic Detector Array
Figure 14: 18mm diameter acoustic sensor with 400 disc elements each with 0.3mm diameter. Side view (left) and top view (right).

## Slide 21
k-Wave set-up
Figure 15: Sensor geometry and proton beam energy deposition in k-Wave simulation with 0.1mm voxels
sensor array
proton beam

## Slide 22
Acoustic Time Series
Figure 16: Acoustic time-series from the data received by the acoustic sensor

## Slide 23
Frequency Spectrum
Figure 17: Frequency spectrum from the data received by the acoustic sensor

## Slide 24
Image Reconstruction: Iterative time-reversal
Figure 18: Reconstructed pressure distribution using an iterative time reversal algorithm