## Slide 1: Sci-Fi plane update
Josie McGarrigle, Anthea MacIntosh-LaRocque, Vania Lay

## Slide 2: Scintillating Fibre plane: prototype 1
2
10mm
Grooves for fibres
Cavities for epoxy resin
Backing plate
Plastic frame
Figure 1: Fibre plane mid-construction
Figure 2: Fibre plane mid-construction side-view
Figure 3: Plane mid-construction with 33 fibres in place
Blu-tack to hold fibres during construction
Scintillating fibres
1 ”top frame” attached to secure fibres

## Slide 3: Scintillating Fibre plane: prototype 2
Grooves for fibres
Planes, 2 on top, 2 underneath
32 fibres
Top plate
Bottom plate
'Well' rather than grooves
Figure 4: Winding jig CAD design with planes
Figure 5: Fibre plane CAD design

## Slide 4: Next Steps
Plane assembling- wrap planes, add resin, add lids.
Test the fibres readout- one-to-one connection between scintillating fibres and clear fibres will be constructed to transport light between and read out the light.
Add to phantom, record readings and fit Bortfeld approximation!

## Slide 5: Liquid Scintillator
Due to worries of potential misalignment, liquid scintillator was proposed.
Water-based solution to put throughout the phantom for uniformity.
Combines the advantages of pure water, including low attenuation, accurate direction reconstruction, and low cost, and those of liquid scintillator, including high light yield and low-threshold detection.
Test both plane and liquid, fit Bortfeld, see which best.