## Slide 1
Minibeam radiation therapy:
from photons to charged particles
Yolanda Prezado, PhD, HDR

## Slide 2: Spatial fractionation of the dose in Radiation Therapy
Standard radiotherapy
< 1 mm
1-2 mm
+
Large beam sizes (> 1 cm2)
Homogeneous
dose distributions
Spatial fractionated radiotherapy
x-rays minibeam radiation therapy
Narrow beam sizes spaced by areas of low dose
+
Heterogeneous distributions
> 1 cm

## Slide 3: Spatial fractionation of the dose in Radiation Therapy
> 1 cm
+
Remarkable increase of normal rat brain resistance.
Dilmanian et al. 2006, Prezado et al., Rad. Research 2015
Dose escalation in the tumor possible higher tumor control
Distinct biological mechanisms not yet understood
Standard RT
Spatial fractionated radiotherapy
x-rays minibeams radiation therapy
Large beam sizes (> 1 cm2)
Homogeneous
dose distributions
< 1 mm
1-2 mm

## Slide 4: SFRT types: GRID/MBRT/MRT
1 cm
MV beams
LINACs
0.6 mm
0.05 mm
GRID therapy
Minibeam RT (MBRT)
Microbeam RT (MBRT)
Mainly kV beams
Origin-> large synchrotrons

## Slide 5: Microbeam Radiation therapy
MRT uses 50 µm-wide beams, spaced by 400 µm
Slatkin et al. Med. Phys. 1992
Differential effect normal tissue versus tumor observed in animal experiments
Normal (brain) is able to withstand
more than 300 Gy/one fraction
Laissue et al, SPIE 2001
Tumor control effectiveness in glioma-bearing rodents
Laissue et al, Int.J. Cancer 1998
600 Gy

## Slide 6: Drawbacks of MRT
Requires extremely high dose rates
Scarce beamtime at synchrotrons
Difficult realization of clinical trials
Not favourable dosimetry (low-energy X-rays)
High doses to control tumors 300-600 Gy.
Good compromise: Minibeam radiation therapy
Dilmanian et al., PNAS 2006

## Slide 7: Minibeam radiation therapy: a good compromise
Beam widths: 500-700 µm; center-to-center distance: beam width x 2
Tumor control in glioma-bearing rats
Deman 2012, Prezado 2012.
Gain in normal tissue sparing
maintained
Doses as high as 100 Gy/one fraction
well-tolerated by rat brain
(Dilmanian 2006, Prezado 2015).
&
Interlacing possible

## Slide 8: Minibeam radiation therapy: a good compromise
8
Beam widths: 500-700 µm  transfer to low cost equipment possible
Prezado & Dos Santos et al. Scie. Reports 2017
8
Gain in normal tissue tolerances
Whole rat brain irradiation (20 Gy average)
Tumor control effectiveness
F98 glioma-bearing rats
Proof of concept

## Slide 9
Moving forward… Proton minibeam radiation therapy (PROTONMBRT)

## Slide 10: PROTONMBRT: an innovative therapeutic approach
Protons and their specific physics and biology
Minibeam radiation therapy
Proton minibeam radiation therapy
Prezado et al. Med. Phys.2013
Tumor
First implementation worldwide at a Orsay proton therapy centre (I. Curie)
(Peucelle, Martinez,… and Prezado, Med. Phys. 2015)

## Slide 11
First evaluation of normal brain response (Prezado et al. Scie. Rep. 2017)
Standard PT (25 Gy/one fraction)
pMBRT (25 Gy average dose-
58 Gy peak dose/one fraction)
Skin: moist desquamation
Permanent epilation
Important brain damage
No skin damage
Reversible epilation
No brain damage observed
No cognitive effects observed
Proton minibeam radiation therapy spares normal brain
Whole brain irradiations (normal rats, 7-weeks old). Long-term follow up (6 m)
VERSUS
NET REDUCTION IN NEUROTOXICITY

## Slide 12: Tumor control effectiveness in glioma (RG2) bearing rats
25 Gy/one fraction
pMBRT  67 % of long-term survivals (free of tumor).
Among the best results ever obtained with radiotherapy alone
Prezado et al., Red Journal 2019
Standard PT
pMBRT
Tumor
Tumor

## Slide 13: pMBRT provides tumor control even with highly heterogeneous dose distributions
INHOMOGENOUS dose distribution
70 Gy in the peak  30 Gy average
Whole brain irradiation, 8 days after implantation (n=10)
Without significant toxicity
Prezado et al. Scie. Reports 2018

## Slide 14
Proton minibeam radiation therapy widens the therapeutic window for gliomas

## Slide 15: Short term objectives (3-5 years)
To reach Phase I/II clinical trials
PROTONMBRT
Proof of concept in
small animals
Clinical trials
ERC consolidator grant (2019-2024)
Generation of intense minibeams at a clinical center
Challenging dosimetry (extremely small field sizes)
Radiobiology
  -To find the physical parameters maximizing the therapeutic index
  -To unravel the biological mechanisms

## Slide 16: Implementation at a clinical PBSPBS
MC (TOPAS) versus IBA nano RAZOR diode
L. De Marzi et al. Med. Phys 2018
6 Gy/min in the peak
Less neutron production

## Slide 17: Dosimetry studies
PTW Microdiamond (61009)
IBA nano-RAZOR diode
High spatial resolution (1 µm) in one direction,
2.2 mm in the others
High spatial resolution (60 µm) in all three dimensions
De Marzi et al. Med. Phys. 2018
PROTONMBRT: an innovative therapeutic approach

## Slide 18: Magnetically focussed proton minibeams at a clinical center
T. Schneider et al. Scientific Reports 2020

## Slide 19
First evaluation of treatment plans
P. Lansonneur et al. Scie. Reports 2020

## Slide 20
Moving forward… Heavy ions minibeam radiation therapy

## Slide 21: Heavy ions MBRT: Advantages
Reduced MSC high PVDR in normal tissue
Narrow beams possible (500 µm)
Gonzalez, Peucelle and Prezado, Med. Phys 2017
Possible synergies of MBRT effects with the higher capacity of ions to inhibit angiogenesis and activate immune system

## Slide 22: Heavy ions MBRT: impact on valleys
Large beam spacing (ctc) minimize
the contribution of high LET fragments to the valleys
Heavier fragments
are dominant in the valleys at the target position, which might favor tumor control.
Gonzalez, Peucelle and Prezado, Med. Phys 2017
Larger Beam spacing
Tumor
Tumor

## Slide 23: Very heavy ions MBRT
Ne, Si and Ar ions used in the past, extremely efficient for the treatment of hypoxic tumors (Castro 1994)
HOWEVER, abandoned due to important side effects in normal tissues
Very heavy ions (low OER) + MBRT (sparing of normal tissue)
Improvement of therapeutic index
Peucelle, Martinez and Prezado, Med. Phys. 2015
Our hypothesis

## Slide 24: Final reflections
The dose delivery method may have an important impact on biological response.
Not need to deposit a lethal dose in each of the tumor cells to kill it.
Non-targeted effects can play a major role in RT treatments
Charged particles (p, heavy ions) allow to fully profit from the advantages of spatially fractionated radiotherapy

## Slide 25: NARA team (former members)
C. Guardiola
C. Lamirault
R. Delorme
T. Schneider
I. Martinez
M. Dos Santos
J. Bergs
C. Peucelle
W. Gonzalez
Acknowledgments
Biology Service of IMNC: M. Juchaux
Acknowledgments

## Slide 26: NARA team
Acknowledgments

## Slide 27: Acknowledgments
IR4M
C. Sebrie
Experimental RT
platform
F. Pouzoulet
D. Labiod
C. Roulin
Orsay Proton
therapy Center
A.Patriarca
L. De Marzi
C. Nauraye
R. Dendale
E. Hierso
Institut Pasteur
G. Jouvion
D. Hardy
Institut Curie

## Slide 28
Thank you very much for your attention!
yolanda.prezado@curie.fr