## Slide 1
Interest of LhARA for innovative RT
Yolanda Prezado
Notes: Lo de las perspectivas

## Slide 2: Radiotherapy: a paradigm shift in the 21th century
TIME
SPACE
ENERGY
PARTICLE
Fractionation
Dose rate
Pulse structure
Standard RT
Photons
Protons
Heavy ions

## Slide 3: Exploration of the influence of the different parameters on the biological response
TIME
SPACE
ENERGY
PARTICLE
Clinical accelerators = non-flexible
Protons/heavy ions facilities= low accessibility
New flexible accelerators are needed

## Slide 4: Laser Hybrid Accelerator for radiobiology applications
G. Aymar et al. Frontiers in Physics
Notes: Nanorain

## Slide 5: Spatially Fractionated Radiation Therapy (SFRT)
Standard RT
SFRT
large fields (≥ 1 cm)
laterally homogeneous dose distributions
field composed of smaller beamlets
laterally heterogeneous dose distributions (peaks and valleys)
➜ increase of normal tissue tolerance
≥ 1 cm
peak valley
beamlet

## Slide 6
Prezado et al. 2013
Tumor
Proton MBRT
Charged particles
Minibeam radiation therapy (MBRT)
PROTONMBRT: an innovative therapeutic approach
ERC consolidator grant
Beam width < 1 mm

## Slide 7: pMBRT increases the therapeutic index for high-grade gliomas
Equivalent or superior tumor (rat glioma) control than standard proton therapy
Prezado et al. IJROP 2019
5 days after IR
26 days after IR
Net reduction of neurotoxicity
pMBRT
Standard
PT
Prezado et al. Scie Reports 2017; Lamirault et al. Scie Reports 2020
necrosis
Inflammation
astrogliosis
demyelination
25 Gy/one fraction

## Slide 8: pMBRT a promising alternative for re-irradiations
Naive Rat’s brain irradiations
N=8/group
Day 0
Conv RT (BB)
20 Gy
Day 60
Conv RT 20 Gy
OR
pMBRT 20 Gy mean dose
Behavioural tests
@ 3 and 6 months after the first IR
Chart: Discrimination ratio
|
Controls | 0.34184
BB | 0.48998
BB + BB | 0.23514
BB + pMBRT | 0.41225
 | Incidence/mean |  |  | 
Main Finding | CTRL | BB+pMBRT | BB+BB | BB
Thalamus: Vacuolation | 0 | 0 | 2/1.0 | 0
Necrosis, fimbria | 0 | 4/1.3 | 5/1.6 | 0
Necrosis, alveus | 0 | 0 | 2/1.5 | 0
Necrosis CA1 to CA4, gyrus denta-tus | 0 | 0 | 3/1.7 | 0
Microthrombi/ossification, plexus | 0 | 0 | 3/1.0 | 0

## Slide 9
PROTONMBRT
Net reduction of normal tissue toxicities
Equivalent or superior tumor control as in conventional RT even with highly heterogenous dose distributions
WHY?

## Slide 10: Immune response generated in (orthotopic) glioblastoma model after pMBRT
T cells are key in pMBRT mechanism
Rats Fischer (immunocompetent)
Rats Nude (immunodeficient)
Athymic rats (Nude)
 Lack T lymphocytes
1 fraction of 25 Gy average in pMBRT
Catherine Sébrié, IR4M
Glioblastoma (RG2)
Bertho, Iturri et al. IJROBP 2022

## Slide 11: Lymphocytes in pMBRT
Infiltration of tumor-associated lymphocytes (TRM T cells and B cells)
Flow cytometry analysis
Control
ConvPT 7dpi
pMBRT 7dpi
Notes: In order to do so, we started by a quantification of the overall immune infiltration in the tumor microenvironment by a flow cytometry analysis. Among 11 different immune cell types analysed, we observed that tumor associated lymphocytes were highly recruited both after conventional protontherapy here in red, and pMBRT in blue. Although specifically CD4 T cells and in the case of pMBRT TRM T cells and B cells)

## Slide 12: Lymphocytes in pMBRT
Infiltration of tumor-associated lymphocytes (TRM T cells and B cells)
Flow cytometry analysis
Control
ConvPT 7dpi
pMBRT 7dpi
RADIOBIOLOGY
Notes: In order to do so, we started by a quantification of the overall immune infiltration in the tumor microenvironment by a flow cytometry analysis. Among 11 different immune cell types analysed, we observed that tumor associated lymphocytes were highly recruited both after conventional protontherapy here in red, and pMBRT in blue. Although specifically CD4 T cells and in the case of pMBRT TRM T cells and B cells)

## Slide 13: Minibeam radiation therapy could provide long-term anti-tumor immunity
Irradiated and cured immunocompetent RG2-bearing rats were rechallenged with RG2 tumor cells 3 to 6 months after irradiation
CTRL
MBRT

## Slide 14: Minibeam radiation therapy leads to a different spatio-temporal recruitment
Center
Adjacent
Periphery
pMBRT induces the recruitment of T cells in the center of the tumor
and B cells in the adjacent tissue and the periphery of GB
Spatial distribution of immune cells
Immunofluorescence
Center
Adjacent
Periphery
T cells
B cells
RADIOBIOLOGY

## Slide 15: MBRT induces a faster recruitment of T cells in the center of the tumor
Notes: These results were similar to a previous publication from our lab, in which we studied in a similar way the immune response after x-ray minibeam radiation therapy.
In this study, not only T cells were more recruited in the center, but the difference was more striking 2 days after the irradiation. Therefore, MBRT induced a faster recruitment of T cells in the center. This suggests that in spatial fractionation immune response is related to a different spatio-temporal recruitment
Although for the sake of comparison, the doses given in the conventional group are

## Slide 16
Immune infiltration of tumors irradiated by MBRT seems to be characterized by increased (and fast) intratumoral T and B cells.
MBRT leads to a distinct spatio-temporal immune recruitment.

## Slide 17: Implementation at a clinical pencil beam scanning systemBS
MC (TOPAS) versus IBA nano RAZOR diode
L. De Marzi et al. Med. Phys 2018
6 Gy/min

## Slide 18: Beam characterics LhARA
Ideal beam features
Low divergence
Small emittance
T. Schneider et al. Scientific Reports 2020
Magnetically focussed minibeams
can pave the way towards combination of pMBRT + FLASH
LhARA  FWHM < 0.5 mm

## Slide 19: Carbon minibeam radiation therapy @ GSI
550 µm width
Conv. IR
MBRT
Single slit
Dose prescription: 20 Gy average
180 MeV/A C ions
Dose peak = 121 ± 6 Gy,
D valley = 1.5 ± 0.1 Gy
Less lung metastasis with Conv.RT and MBRT
LM8 mice osteosarcoma

## Slide 20: Very heavy ions MBRT
Ne, Si and Ar ions used in the past, extremely efficient for the treatment of hypoxic tumors (Castro 1994). HOWEVER, abandoned due to important side effects in normal tissues
Ne MBRT @ HIMAC, mice’s legs irradiation
MBRT leads to a net reduction of toxicity as compared to BB
Potential renewed use of very heavy ions for therapy!
Prezado et al Cancers 2021
Conv RT
MBRT

## Slide 21: NeMBRT: tumor control delay
SCVii bearing mice, advanced tumors
20 Gy mean dose, 1 Gy valley dose
Broad beam animals reached toxicity endpoints.
Significant tumor growth delay after NeMBRT

## Slide 22: Missing the full picture

## Slide 23: LhARA
Notes: Nanorain

## Slide 24: FLASH radiation therapy (FLASH-RT)
Ultra-fast delivery of radiation
  > 40 Gy/s
  High dose given in milliseconds
Protective effect in healthy tissue: FLASH effect
  Neurocognitive sparing of memory Montay-Gruel 2017
  Reduction in pulmonary fibrosis Favaudon 2014
  Skin, intestine, muscle Diffenderfer 2020 & Cunningham 2021 & Tinganelli 2022
Observed with low energy electrons (mostly), photons, protons and carbon ions
R. Ortiz (NARA)
Most direct traslation

## Slide 25: Mechanisms?
From Montay-Gruel 2019
Oxygen depletion: significant intracellular O2 dropcontroversial
ROS and free radical from peroxidation reduced in normal cells
Modulation of immune response

## Slide 26: On the impact of anesthesia’s O2
Important open question in brain radiotherapy: the impact of oxygen content in gas anaesthesia and radiation dose rate on normal tissue tolerance of brain radiotherapy.
This is a particularly relevant clinical question in paediatric oncology.
Adolescent Fischer rats, brain irradiation, 25 Gy
Notes: Nature Comm. Under revision

## Slide 27: On the impact of anesthesia’s O2
Detrimental effect of anesthesia’s O2 in both CPT and pFLASH irradiations, being in the latter case where the most extensive brain damage is observed. the benefit/risk strategy of high or low dose oxygen administration will need to be discussed and a balance struck between issues of safety and therapeutic outcome /toxicity of radiation therapy.
Iturri et al. Nature Comm. accepted

## Slide 28: Pulsed Radiobiology

## Slide 29: LhARA will open new a wide range of possibilities for exploration
Evaluation of the influence of different fractionation schemes in SFRT
Optimised spatiotemporal dose distributions
Influence of the particle type
Assessment on the (ultra high) dose-rate dependance in SFRT
Set of irradiation parameters to achieve a robust FLASH effect

## Slide 30
Thank you very much for your attention!
yolanda.prezado@curie.fr